## Slide 1
IP Interconnection Profile
Consensus Points
6/17/2014

## Slide 2: Protocol Technical Items
Carrier's MUST support the History-Info Header and SHOULD support of the SIP Diversion header for a period of time in order facilitate interoperability.
  When both headers are sent, the sender MUST ensure that they are semantically identical.
Carrier's May support redirection across the NNI, based on bilateral agreement. The redirection MAY be performed with a 3XX or REFER message.
Carrier's MUST support P-Early-Media as defined in RFC 5009.
Resource Priority Header (RPH) MUST be supported by NS/EP compliant networks, and MUST be transparently passed by non-NS/EP compliant networks.
  VOICE-ADMIT Forwarding Per-Hop Behaviour per RFC 5865

## Slide 3: Protocol Technical Items
Specified the exact presentations of Fully Qualified Domain Names in “From:”, “To:” and “PAI” fields.
The originating Carrier network MUST provide the calling number of the originating user in the P-Asserted-Identity header field of dialog-initiating requests.
If the originating user wants to remain anonymous, the originating Carrier network MUST include a Privacy header field containing the value "id" as specified in [RFC 3323] and [RFC 3325].

## Slide 4: Protocol Technical Items
Carrier's MUST support SIP Overload Control with mandatory support of the default algorithm, for SIP congestion control. Carrier's MAY optional support the Rate Based algorithm based on bilateral agreement between two carriers.
  Government Priority Services are exempt from overload controls
An Carrier network MAY impose limits on the number of simultaneous calls, and the incoming rate at which it will accept calls, from a peer. On receiving a dialog-initiating request that exceeds such limits, the receiving Carrier network MUST respond with a 503 (Service Unavailable) response.
An Carrier network MAY periodically send an OPTIONS request containing a Max-Forwards header field set to a value of '0' to detect the availability of a peer’s ingress point.

## Slide 5: Protocol Technical Items
Distinguishing traffic classes
  In order to distinguish between traffic classes, the use of the DSCP marking scheme in Behavior Aggregation mode
  Same DSCP for Voice and Media
  VOICE-ADMIT Forwarding Per-Hop Behavior per RFC 5865 for NS/EP traffic
It is the responsibility of the IPv6 Carrier network to perform the IPv4/IPv6 interworking function when interworking with an IPv4 Carrier network.
Peer Carrier networks SHOULD support the RTP Loopback Test procedures
  Carrier networks that support the RTP Loopback procedures will provide a SIP URI that identifies a media endpoint within the Carrier network that performs the loopback functions.
  Ideally, this "loopback" media endpoint would be located near the ingress point of the peer Carrier network.

## Slide 6
Mandatory and optional narrowband and wideband codecs, including codec/packetization period use and transcoding guidelines

## Slide 7: Security
The VoIP traffic, from the border element in one carrier’s domain to the border element in another carrier’s domain, shall be secured, either physically or logically, from Internet Transit traffic.
This security can be achieved:
  physically: by implementing separated and dedicated networks for the traffic.
  logically: by implementing mechanism such as Virtual Private Networks (either layer 2, e.g., VLANs, or layer 3, e.g., MPLS-VPN) and Tunneling (e.g. IP Sec).