Contribution

TITLE: Text to be added after existing text in Section 4 of the IP Interconnection Routing document (IPNNI-2014-00064R002) which describes a generic process for establishing IP interconnection between service providers using the aggregate approach.

SOURCE*: Neustar, Tom McGarry; NetNumber, Doug Ranalli

_______________________________

ABSTRACT

There are two broad steps to establishing IP interconnection between service providers:

- Establishing the network connection between the SBCs

- Setting up service provider specific routing information to that connection

# Establishing the Network Connection

Establishing the network connection is a process that occurs between the network engineers of each service provider.  There are four steps in this process:

- Exchange end point information of the SBCs – this is in the form of IP addresses or domain names

NOTICE

_____________________________________________________________________________________________

This is a draft document and thus, is dynamic in nature. It does not reflect a consensus of the ATIS-SIP Forum IP-NNI Task Force and it may be changed or modified. Neither ATIS nor the SIP Forum makes any representation or warranty, express or implied, with respect to the sufficiency, accuracy or utility of the information or opinion contained or reflected in the material utilized. ATIS and the SIP Forum further expressly advise that any use of or reliance upon the material in question is at your risk and neither ATIS nor the SIP Forum shall be liable for any damage or injury, of whatever nature, incurred by any person arising out of any utilization of the material. It is possible that this material will at some future date be included in a copyrighted work by ATIS or the SIP Forum.

* CONTACTS:

Tom McGarry, Neustar, tom.mcgarry@neustar.biz, 571-434-5570

Doug Ranalli, NetNumber, dranalli@netnumber.com, 978-848-2830

- Exchange security credentials – examples include user name/password and digital certificates, this will be used to establish a secure connection between SBCs such as an SSL or VPN connection

- Establish agreed to parameters for the connection, such as bandwidth constraints

- Create and name the SIP trunk group (SIP TG) between the SBCs that identifies this connection – this is how the SBC identifies the connection, (the SIP TG is sometimes referred to as a session agent)

# Setting Up Routing

Setting up routing involves associating route identifiers provided by the terminating network with the appropriate SIP TG in the originating network that is to be used for reaching the endpoints.  There are many choices for what routing identifiers can be used including; AOCN/OCN, NPAC SPID, CO code, 10-digit telephone number, domain name and SIP URI.

There are three steps in this process:

- The terminating carrier provides a list of route identifiers to the originating carrier and the network entry-point(s) to be used for routing calls to each identifier.

- The originating carrier establishes a process during call setup (such as a dip to a route server) to create a URI that often includes destination trunk group parameters as per RFC 4904 and portability parameters as per RFC 4694.  To do this, the originating carrier will (1) portability-correct the dialed digits, (2) associate the portability corrected digits with a route identifier and (3) identify the SIP TG based on the route identifier.  The original dialed-digits, portability-data, outbound SBC and trunk-group are typically identified in the URI that is used to route the call/session.  For example:

  - sip:+12125551234;npdi;tgrp=1234;trunk-context=origin.tld@outbound_sbc.origin.tld;user=phone

- The originating carrier routes the call/session to the interconnected carrier based on the SIP TG identified in the URI.