## Slide 1: Routing Considerations
The ideas in this presentation are offered for discussion only.
  Reality is undoubtedly far more complicated…
This presentation attempts to explore the question of whether or not data can be automatically synchronized between the “routing data” options:
  Between Per-TN solutions?
  Between Aggregate solutions?
  Per-TN  Aggregate?

## Slide 2: Per TN Routing Considerations
Synchronization between ENUM databases is well understood.
Synchronization between ENUM and NPAC (for URI data) may be possible:
  NPAC => ENUM is straightforward
  ENUM => NPAC – some restrictions apply
Synchronization between ENUM and other per-TN databases should be possible:
  Mapping may be required
  If either database applies policy, the mapping could be complex – otherwise may be straightforward.

## Slide 3: NPAC  ENUM
NPAC
(authoritative for number portability)
Porting Request
ENUM
(Alternate Registry)
All changes sync
To change information in NPAC, ENUM registry would need to use interface currently used by service providers, would need to be authorized to do so.
IP-NNI routing change
Changes would be limited to numbers “owned” by a given service provider. Other restrictions might apply.
Allows “registries” to co-exist with simple well defined rules
Synchronization is applied without policy
Service providers can add policy filter within their own networks (allows each service provider to make their own decisions).
This might require new rules, new interfaces, or perhaps both.
This should be the easy piece.

## Slide 4: NPAC  ENUM
NPAC
(authoritative for number portability)
Porting Request
ENUM
(Alternate Registry)
All changes sync
To change information in NPAC, ENUM registry would need to use interface currently used by service providers, would need to be authorized to do so.
IP-NNI routing change
This might require new rules, new interfaces, or perhaps both.
This should be the easy piece.
Other “registry”
Fully synchronizes with ENUM registry.
Rules for synchronizing with NPAC are the same as for ENUM with NPAC
Only the number owner can make changes to IP-NNI routing info.

## Slide 5: Information to Synchronize
NPAC
(authoritative for number portability)
Porting Request
ENUM
(Alternate Registry)
All changes sync
To change information in NPAC, ENUM registry would need to use interface currently used by service providers, would need to be authorized to do so.
IP-NNI routing change
This might require new rules, new interfaces, or perhaps both.
This should be the easy piece.
Other “registry”
Fully synchronizes with ENUM registry.
Rules for synchronizing with NPAC are the same as for ENUM with NPAC
Only the number owner can make changes to IP-NNI routing info.
Key Questions:
What is the core information that would be synchronized?
Can we agree on the data fields?
Can the contribution from Chris Wendt be used as a starting point?

## Slide 6: Aggregate => Per-TN
NPAC
(authoritative for number portability)
Porting Request
ENUM
(Alternate Registry)
All changes sync
To change information in NPAC, ENUM registry would need to use interface currently used by service providers, would need to be authorized to do so.
IP-NNI routing change
Other “registry”
Fully synchronizes with ENUM registry.
Rules for synchronizing with NPAC are the same as for ENUM with NPAC
Only the number owner can make changes to IP-NNI routing info.
“Virtual Registry”
Aggregate methods based on PSTN constructs are expanded out for every TN
This can then be synchronized with the other registry by anyone who wants to do so (no obligations on anyone)
Logically this is nothing more than a TN = SIP URI list
…
LERG
Spreadsheet
Napkin

## Slide 7: Per-TN => Aggregate
NPAC
(authoritative for number portability)
Porting Request
ENUM
(Alternate Registry)
All changes sync
To change information in NPAC, ENUM registry would need to use interface currently used by service providers, would need to be authorized to do so.
IP-NNI routing change
Other “registry”
Fully synchronizes with ENUM registry.
Rules for synchronizing with NPAC are the same as for ENUM with NPAC
Only the number owner can make changes to IP-NNI routing info.
“Virtual Registry”
Could “per-TN” providers also provide an alternate interconnection point for each TN that can be stated as a simple rule? E.g.,
  Route everything to one interconnect
  NNX => URI
  Etc.
Input into service provider provisioning systems

## Slide 8: Questions
Is it worth exploring the technical feasibility of mechanisms that could automatically synchronize routing data between different solutions?
Should a discussion of these mechanisms be part of the Routing TR?
Would there be value in proof-of-concept testing of these mechanisms in a numbering testbed?