Contribution

TITLE: Use of Additional Resource Records in ENUM Query Response – edit to Routing Report

SOURCE*: AT&T, Penn Pfautz

_______________________________

ABSTRACT

This document proposes additional text added to Section 5.2 of the Routing Report.

NOTICE

This is a draft document and thus, is dynamic in nature. It does not reflect a consensus of the ATIS-SIP Forum IP-NNI Task Force and it may be changed or modified. Neither ATIS nor the SIP Forum makes any representation or warranty, express or implied, with respect to the sufficiency, accuracy or utility of the information or opinion contained or reflected in the material utilized. ATIS and the SIP Forum further expressly advise that any use of or reliance upon the material in question is at your risk and neither ATIS nor the SIP Forum shall be liable for any damage or injury, of whatever nature, incurred by any person arising out of any utilization of the material. It is possible that this material will at some future date be included in a copyrighted work by ATIS or the SIP Forum.

* CONTACT: Penn Pfautz; email: pp3129@att.com; Tel: +1732-420-4962

As discussed in ATIS/SIP Forum IP NNI Task Force contribution IPNNI-2014-00107R001, the response to an ENUM query during call set up can contain addition DNS resource records that can be used to simplify the complexity of IP interconnection routing provisioning and the need for offline data exchange when network changes are made. This contribution adds the following text to the end of Section 5.2 (NPAC as a Tier 1 ENUM Registry) of the Routing Report to note this possibility:

In response to the ENUM query, the Tier 2 name server may also provide additional DNS resource records. These records could provide SBC IP address information to resolve the URI hostname, obviating the need for this information to be exchanged offline and for the information to be updated should additional SBCs be added or traffic migrated to different SBCs. In addition to such address (A and AAAA) records, SRV records could be provided. SRV records could support the implementation of different routing disciplines (e.g., proportional and/or ordered routing among a set of ingress SBCs) as some IP traffic exchange routing plans already require, without the need for a service provider to build translations for different, potentially elaborate, routing plans for each partner carrier.

# Footnotes

Other solutions involving an ENUM query of the destination SP during call set up can also support these capabilities.