## Slide 1: STI and Call-Forwarding
Chris Wendt (Comcast)
David Hancock (CableLabs)

## Slide 2: Mainline STI Sequence
UE-a
TN-a
SP-a
SP-b
UE-b
TN-b
[1] INVITE TN-b
[2] INVITE TN-b
[3] INVITE TN-b-contact
PAI:TN-a; To:TN-b; Date: t
Calling Number verified
PAI:TN-a; To:TN-b; Date: t
Identity:
ppt=shaken
attest=full
orig/dest/date=a/b/t
signature=E(a,b,t)
info = SPa-cert-URL 
To:TN-b; Date: t
Calling identity verification passes

## Slide 3: Interactions between STI and Call Forwarding
Current behavior
  Some call features such as call-forwarding can update SIP header information covered by the Identity signature
  Result: generates false-negative verification output
Two call-forwarding examples
  MMTEL TAS updates To header to hide identity of forwarding user when privacy enabled (per TS 24.604)
  SIP-PBX call-forwarding may update To header (for privacy), and may update PAI header (per SIPconnect 2.0)
Recommended action
  Adopt PASSporT “div” extension defined in draft-peterson-passport-divert
  This extension signs forwarding user identity for each forwarding leg

## Slide 4: TAS/MMTEL Call Fwd’ing (privacy enabled) causes false negative verification failures
UE-a
TN-a
SP-a
SP-b
SP-c
UE-c
TN-c
TN-b CFW to TN-c (private)
[1] INVITE TN-b
[2] INVITE TN-b
[3] INVITE TN-c
PAI:TN-a; To:TN-c; Date: t
Identity:
[4] INVITE TN-c Contact
PAI:TN-a; To:TN-b; Date: t
Identity:
PAI:TN-a; To:TN-c; Date: t
Calling Number Not Verified
ppt=shaken
attest=full
orig/dest/date=a/b/t
signature=E(a,b,t)
info = SPa-cert-URL 
ppt=shaken
attest=full
orig/dest/date=a/b/t
signature=E(a,b,t)
info = SPa-cert-URL 
Update To header to hide fwd’ing user’s identity
Calling identity verification fails
Received To header doesn’t match To header used to build Identity signature

## Slide 5: PBX Call-Fwd’ing (privacy enabled) downgraded to “Gateway” attestation
UE-a
TN-a
SP-a
SP-b
PBX-B
SP-c
TN-b CFW to TN-c (private)
[1] INVITE TN-b
[2] INVITE TN-b
[3] INVITE TN-b
From:TN-a; PAI:TN-a; To:TN-b; Date: t
Identity:
From:TN-a; PAI:TN-a; To:TN-b; Date: t
Identity:
[4] INVITE TN-c
From:TN-a; PAI:TN-b; To:TN-c; Date: t
Identity:
[5] INVITE TN-c
ppt=shaken
attest=full
orig/dest/date=a/b/t
signature=E(a,b,t)
info = SPa-cert-URL 
(same)
(same)
From:TN-a; PAI:TN-b;
To:TN-c; Date: t
Identity:
Update To to TN-c
Update PAI to TN-b
Identity header verification yields a “Not Validated” result, since To header was updated by PBX.
Therefore, SP-b downgrades Identity attestation to “gateway” in [5].
ppt=shaken
attest=gateway
etc…

## Slide 6: PASSporT “div” extension – draft-peterson-passport-divert
Overview
  Base PASSport token contains three claims; “orig”, “dest”, and “iat”
  PASSporT “div” extension adds a 4th “div” claim containing the forwarding user identity
Sequence
  Originating Service Provider adds Identity header containing the base PASSporT token
  Each forwarding Service Provider adds a new Identity header containing a “div” PASSporT token containing a signature across the following claims:
    “orig” contains calling user identity
    “div” contains forwarding user identity
    “dest” contains forward-to user identity
    “iat” contains Date timestamp
  When terminating SP receives an INVITE containing a base Identity header and one or more “div” Identity headers
    It walks through the chain of forwarding events to verify the identity of each forwarding user

## Slide 7: Example Message Sequence for PASSporT “div” Extension
UE-a
TN-a
SP-a
SP-b
SP-c
UE-c
TN-c
TN-b CFW to TN-c (privacy enabled)
[1] INVITE TN-b
[2] INVITE TN-b
[3] INVITE TN-c
PAI:TN-a; To:TN-c; Date: t
Identity:
Identity:
[4] INVITE TN-c Contact
ppt=shaken
attest=full
orig/dest/date=a/b/t
signature=E(a,b,t)
info = SPa-cert-URL 
PAI:TN-a; To:TN-b; Date: t
Identity:
ppt=shaken
attest=full
orig/dest/date=a/b/t
signature=E(a,b,t)
info = SPa-cert-URL 
PAI:TN-a; To:TN-b; Date: t
Calling Number Verified
ppt=div
orig/div/dest/date=a/b/c/t
signature=E(a,b,c,t)
info = SPb-cert-URL 
Forwarding SP-b adds 2nd Identity header supporting “div” extension