## Slide 1: STI Interworking with SIP-PBXs
Chris Wendt (Comcast)
David Hancock (CableLabs)

## Slide 2: Applying STI to Multi-homed SIP-PBX
Service Provider 1
SIP-PBX
Service Provider 2
SP-1 TNs
SP-2 TNs
TN-a TN-b TN-c
…
TN-1 TN-2 TN-3 …
INVITE TN-x
Problem Description
SP-1 and SP-2 each assign a set of TNs to PBX
PBX initiates a call via SP-2 with calling TN belonging to SP-1
SP-2 sends INVITE on to SP-x owner of called TN-x
Problem: In step-3, how does SP-2 create Identity signature for a calling TN that it does not own?
Service Provider x
PAI:TN-1; To:TN-x; Date: t
INVITE TN-x
???
PAI:TN-1; To:TN-x; Date: t
Identity:
1
2
3

## Slide 3: One Solution Approach – have PBX sign calling identity
Service Provider 1
SIP-PBX
Service Provider 2
SP-1 TNs
SP-2 TNs
TN-a TN-b TN-c
…
TN-1 TN-2 TN-3 …
INVITE TN-x
Service Provider x
ppt=shaken
attest=full
orig/dest/date=1/x/t
signature=E(1,x,t)
info = Cert-URL 
PAI:TN-1; To:TN-x; Date: t
Identity:
INVITE TN-x
ppt=shaken
attest=full
orig/dest/date=1/x/t
signature=E(1,x,t)
info = SPa-cert-URL 
PAI:TN-1; To:TN-x; Date: t
Identity:
1
2
3
Solution Description
SP-1 and SP-2 allocate TNs to PBX.
PBX adds Identity header containing signature of calling TN-1 in INVITE to SP-2.
SP-2 verifies received Identity signature, and if valid, it replaces received Identity with new Identity containing SP-a generated signature of calling TN-1.
Question: How does PBX generate signature for calling TN?

## Slide 4: Two Solution Options
Option-1:
  PBX obtains Identity Identity header from the host SP that owns the calling TN
Option-2
  PBX generates Identity header using certificate and private key obtained from host SP that owns calling TN

## Slide 5: Option-1: PBX obtains Identity Header from SP
PA/CA
SP STI Functions
(KMS, SKS, AS, etc.)
SP-1
SIP-PBX
Public STI
Call Control
[2] Sign TN-1
[3] Identity <TN-1>
SP-2
Call Control
[4] INVITE
Identity: <TN-1>
[1] Orig call request
Architecture
SP hosts a TN signing service that PBX invokes per call.
Message Sequence
PBX user TN-1 initiates DOD call
PBX asks SP-1 to sign calling TN-1 (since SP-1 owns TN-1).
SP-1 returns Identity header containing signature for TN-1
PBX includes received Identity header in INVITE to SP-2. SP-2 verifies Identity signature.
SP-2 sends INVITE to terminating network, containing either received Identity header, or newly created Identity header.
Pros:
  Leverages already-supported signing functionality of Service Provider
Cons:
  Uses resources of Service Provider (per-call)
[5] INVITE
Identity: <TN-1>

## Slide 6: Option-2: PBX generates Identity Header
SP-1
SIP-PBX
Call Control
SP-2
Call Control
[6] INVITE
Identity: <TN-1>
Architecture
SP provides an STI Proxy service to PBX
Message Sequence
PBX user TN-1 initiates DOD call
PBX asks PBX STI Function to sign calling TN.
PBX STI Function sends certificate request to STI Proxy.
STI Proxy returns certificate to PBX STI Function. This cert could be a child of a certificate that SP-1 had previously obtained from the CA. This new child cert could specify PBX-unique attributes, such as the cert lifetime, the set of TNs covered by cert, etc.
PBX STI function returns Identity header to Call Control.
and 7) Same as option-1; PBX includes received Identity header in INVITE to SP-2, etc.
Pros: Avoids use of real-time resources in Service Provider.
Cons: Adds STI functionality to PBX
[7] INVITE
Identity: <TN-1>
PA/CA
PBX STI Functions
(KMS, SKS, AS, etc.)
Public STI
STI Proxy
[1] Orig call request
[3] Get Cert
[4] <cert>
[2] Sign TN-1
[5] Identity <TN-1>