## Slide 1: Identity header Security Review
Chris Wendt (Comcast)
David Hancock (CableLabs)

## Slide 2: Addressing concern of sending Identity header outside SP network
We’ve previously discussed whether or not a host SP should send Identity header to the PBX
  The stated reason for not sending  the untrusted PBX is a potential replay-attack entry point
  Is this really a concern – can a PBX actually replay an Identity in order to get a "verification passed" for a spoofed calling TN?
What actually happens in a pre-"div" SHAKEN-compliant network?
  If PBX replays within "iat" freshness window, then verification service ignores Identity header since "dest" TN doesn’t match R-URI TN
  If PBX replays outside of "iat" freshness window, then verification fails because "iat" is stale

## Slide 3: Example call flow – PBX replays received Identity header (pre-"div” SHAKEN)
PAID:TN-a; To:TN-b; Date: t
Identity: PASSporT token {
orig/dest/iat=a/b/t}
SP-b
SP-x
[1] INVITE TN-b
SP-a
PBX-1
[2] INVITE TN-b
UE-x
TN-x
[3] INVITE TN-x
PAID:TN-a; To:TN-b; Date: t
Identity: PASSporT token orig/dest/iat=a/b/t}
[4] INVITE TN-x
PAID:TN-a; To:TN-b; Date: t
Identity: PASSporT token {orig/dest/iat=a/b/t}
[5] INVITE TN-x Contact
PAID:TN-a; To:TN-b; Date: t
(no Verstat indication)
PAID:TN-a; To:TN-b; Date: t
Identity: PASSporT token {orig/dest/iat=a/b/t}
Replay within "iat" freshness window
Ignore, since R-URI/dest TNs don’t match

## Slide 4: Conclusion and Recommendations
Avoid FUD – Trust STIR
PBX cannot replay Identity header in order to obtain a "verification passed" for spoof calling TN
  Fundamental STIR replay prevention mechanisms apply
Therefore, an SP should not be afraid to send an Identity headers to PBXs, or anywhere outside their network
  Divulging an Identity header is not "giving away the keys to the kingdom"