## Slide 1: Proposal for Change/Improvements in STIR/SHAKEN Technical Report on SHAKEN APIs for a Centralized Signing and Signature Validation Server

## Slide 2: “iat” Content
“iat” is “issued at” Claim
  It pertains to PASSPorT token, i.e. it needs to contain the time when it is constructed
RFC7519 JSON Web Token (JWT )
  Arguably the “most authoritative” specification regarding “iat” content
  4.1.6. "iat" (Issued At) Claim
  The "iat" (issued at) claim identifies the time at which the JWT was issued. This claim can be used to determine the age of the JWT. Its value MUST be a number containing a NumericDate value. Use of this claim is OPTIONAL.
  This text clearly states that “iat” should be populated with the generation time of JWS.
6.1 Datatype: signingRequest
  “Issued At Claim”: Should be set to the date and time of issuance of the PASSporT Token.
  This is how it should to be populated.
8.1.1 Functional Behavior
  The “iat” parameter is populated using the “Date” header field in the SIP Invite. If there is no “Date” header field in the SIP Invite, a Date header field is added to the SIP INVITE.
  Contradicts RFC7519 and 6.1
RFC8244/8225 also needs to be modified regarding content of “iat”
Start of session (which Date header is based on) and PASSPorT generation are temporarily not necessarily close
  Example: PASSPorT generated just before session is routed to a partner network after announcement/digit collection.
  This could introduce a non-negligible artificial drift and cause freshness check issues during validation.
  A new JWS claim should be used if Date needs to be validated as well.

## Slide 3: STI-AS/VS Overload
A signing/verification request associated with a real time session setup procedure needs to complete in a given time frame.
Current HTTP overload control relies on using 503 with a Retry-After header indicating for how long no request should be sent to a server.
  This, although sufficient for certain applications, does not always provide satisfactory results as it allows only binary control of the load following a step function pattern.
  TCP congestion window does not address this issue either as it does not allow an application direct control and is impacted by network conditions like latency, jitter, packet loss.
A mechanism is needed to efficiently deal with STI-AS/VS overload
Similar phenomena is observed for other protocols as well.
  For example, for SIP the issue is addressed by defining a specific mechanism in RFC 7339
  Same overall strategy can be used for HTTP as well
  Server indicates “drop rate” in 503 responses
  https://tools.ietf.org/html/draft-asveren-dispatch-http-overload-control-00
    Work in progress and needs improvements, e.g. clarification about scope, retrying requests, introducing “validity time” parameter.

## Slide 4: verstat, P-Attestation-Indicator, P-Origination-ID
Attestation is not necessarily TN specific
  Is applicable/could be used for other other (non P-Asserted-Identity) as well, e.g. RPH.
  Therefore, verstat, P-Attestation-Indicator, P-Origination-ID should be defined accordingly
verstat
  Possible values shouldn’t be TN-specific
  TN-Validation-Passed  Validation-Passed
P-Attestation-Indicator
  May be different for different headers
  Define as a parameter to be added to the relevant header
P-Origination-Id
  May be different for different headers
  Define as a parameter to be added to the relevant header