## Slide 1: Reference Architecture and Call Flow Example for SIP RPH Signing
Ray P. Singh
ATIS IPNNI Task Force
August 07, 2018
formerly Applied Communication Sciences

## Slide 2: Overview
Proposed Functional Architecture for SIP RPH Signing
  Leverage the SHAKEN infrastructure being implemented by carriers for Telephone Number (TN) signing specified in ATIS-1000074 where feasible
SIP RPH Call Flow Example
  Highlight RPH signing aspects in a typical NS/EP NGN-PS call flow

## Slide 3: Background: SHAKEN Reference Model [ATIS-1000074] Telephone Number Signing
SIP UA: SIP User Agent
CSCF: IMS/Call Session Control Function
IBCF/TrGW: Interconnection Border Control Function/Transition Gateway
STI-AS: Secure Telephone Identity - Authentication Service
STI-VS: Secure Telephone Identity - Verification Service
CVT: Call Validation Treatment
SKS: Secure Key Store
TN-CR: Telephone Number Certificate Repository (TN-CR)

## Slide 4: Proposed Reference Model for RPH Signing
CSCF
SIP UA
SBC-I
(IBCF/TrGW)
TAS/ NS/EP NGN-PS AS
STI-AS
RPH - AS
SKS
SIP
RTP
HTTPS
SIP
SIP
SIP
SIP
CSCF
SIP UA
SBC-I
(IBCF/TrGW)
STI-VS
CVT
SIP
RTP
HTTPS
SIP
SIP
SIP
SIP
TAS/NS/EP NGN-PS AS
RTP
SIP
RPH - VS
Certificate provisioning service
Certificate provisioning service
Service Provider A
(NS/EP NGN-PS Origination/Authentication)
Service Provider B
(NS/EP NGN-PS Termination/Verification)
IPNNI
TAS: Telephone Application Server SBC-I: Session Border Controller - Interconnection
NS/EP NGN-PS AS: NS/EP NGN-PS Application Server RPH-AS: RPH Authentication Service
RPH-VS: RPH Verification Service IPNNI: IP Network-to-Network Interconnection

## Slide 5: Call Flow: IPNNI Origination (Voice & Video)
Prevent PPT from jumping to next slide
P-CSCF
S-CSCF
/I-CSCF
TAS / NS/EP NGN-PS AS
HSS
UE
Prior Condition: Originating UE registered and subscribed to NGN-PS (i.e., GETS-FC service)
1. INVITE
2. INVITE
4. UDR
5. UDA
Optional query for subscription info
EPS
PCRF
Term NW
14. AAR
3. INVITE
Authorization and Service control.
If authorized, the AS removes FC from Request URI and inserts Service User’s Priority Level in RPH wps namespace and aligns ets namespace
PCRF determines QoS-Information for audio and video based on MPS-ID, Reservation-Priority and available ARPs for NS/EP
17. PRACK, 200 OK (PRACK)
ets.x
ets.x wps.y
ets.x
DRMP
6. INVITE
9. INVITE
ets.x wps.y
10. 183 Progress
MPS ; R-P ; DRMP
11. 183 Progress
12. 183 Progress
ets.x wps.y
ets.x wps.y
ets.x wps.y
13. 183 Progress
ets.x wps.y
15. AAA
16. 183 Progress
19. UPDATE, 200 OK (UPDATE)
20. Remaining SIP message exchanges: 180 RINGING, PRACK, 200 OK (PRACK), 200 OK, ACK
Audio, Video Media Bearers
18. Media Bearer Establishment
ppt [rph:"auth“]
Call identified as inter-network and sent to RPH-AS for signing
Includes RPH provisioned ets.x
RPH-AS
7. INVITE
ets.x wps.y
8. INVITE
ets.x wps.y
ppt [rph:"auth“]
RPH is signed using PASSPorT type “rph” and included in SIP Identity Header
Note, call flow is clipped,
But that portion not needed for this presentation

## Slide 6: Call Flow: IPNNI Termination (Voice & Video)
Prevent PPT from jumping to next slide
P-CSCF
HSS
TAS / NS/EP NGN-PS AS
RPH-VS
UE
Prior Condition: Terminating UE registered
1. INVITE
EPS
PCRF
Orig NW
9. AAR
PCRF determines QoS-Information for audio and video based on MPS-ID, Reservation-Priority and available ARPs for NS/EP
11. PRACK, 200 OK (PRACK)
2. INVITE
7. INVITE
8. 183 Progress
MPS-ID ; R-P ; DRMP
11. 183 Progress
12. 183 Progress
ets.x wps.y
10. AAA
13. UPDATE, 200 OK (UPDATE)
14. Remaining SIP message exchanges: 180 RINGING, PRACK, 200 OK (PRACK), 200 OK, ACK
Audio, Video Media Bearers
12. Media Bearer Establishment
Call sent to RPH-VS for verification
S-CSCF/
I-CSCF
3. INVITE
ets.x wps.y
ets.x wps.y
ppt [rph:"auth“]
Validation is successful and Invite is forwarded within terminating network with RPH
ets.x wps.y
ppt [rph:"auth“]
ets.x wps.y
4. LOC_QUERY
5. LOC_QUERY RESP
6. INVITE
ets.x wps.y
Note, call flow is clipped,
But that portion not needed for this presentation

## Slide 7
Thank You