## Slide 1: SIP RPH and TN Signing Cross Relationship
Ray P. Singh
ATIS IPNNI Task Force
October 23, 2018
formerly Applied Communication Sciences

## Slide 2: Overview
General Considerations
  TN signing using SHAKEN and SIP RPH signing for NS/EP NGN-PS need to coexist in a efficient manner
  RPH Signing Considerations
    The “rph” claim token includes the originating TN and destination TN because of the defined structure specified for PASSPorT - Example “rph” Claim Format
          {
          "orig":{"tn":"12155550112"},
          "dest":{["tn":"12125550113"]},
          "iat":"1443208345",
          "rph":{"auth":["ets.0", "wps.0"]}
          }
    Therefore, changes to the “orig” and/or “dest” means any original signed claim must be discarded and new claim issued
  Need to determine handling of cross relationship issues
Following use cases illustrates cross relationship between TN and RPH signing for the purpose of identifying issues

## Slide 3: TN and RPH Signing Use Case Examples
 | Use Case | Description
1 | Basic Access Number (AN) Call | TN and RPH Signing of AN Call
2 | Basic Feature Code (FC) Call | TN Signing of FC+DN Call
3 | FC+AN Call | TN and RPH Signing of FC+AN Call
4 | GETS-NT or AN+GETS-PDN Call | TN and RPH Signing of GETS-NT or AN+GETS-PDN Call
5 | Call Termination in non-NS/EP NGN-PS Network | TN and RPH Signing for terminating in a non-NS/EP NGN-PS SP network
Note: For simplicity only the SIP Invites going across IPNNIs are shown in the following illustrative diagrams

## Slide 4: Use Case 1: TN and RPH Signing of AN Calls
Originating LEC
Originating NS/EP NGN-PS Provider
Transit NS/EP NGN-PS Provider
Terminating NS/EP NGN-PS Provider
UE
UE
1. Invite
2. Invite
ppt [rph:"auth“]
ets.x wps.y
ets.x
ets.x wps.y
ppt [rph:"auth“]
3. Invite
4. Invite
5. Invite
Originating LEC | Originating NS/EP NGN-PS Provider | Transit NS/EP NGN-PS Provider | Terminating NS/EP NGN-PS Provider
LEC is not NGN-PS Service Provider: GETS-AN origination identified as NS/EP based on dialed digits and routed to NS/EP NGN-PS Service Provider TN is signed (SHAKEN process) RPH is NOT signed | NS/EP Service Provider: Performs normal NS/EP NGN-PS processing (including PIN validation) RPH of outgoing SIP Invite is signed using PASSPorT extension and included in a SIP identity header. Received signed TN is discarded Option: Sign new TN in separate identity header or new TN is not signed separately? | Transit NS/EP NGN-PS Provider: May validate the signed RPH to determine whether Invite is forwarded within transit network with RPH If validation is successful, Invite is forwarded within transit network with the RPH If validation is not successful decision to (a) strip RPH or (b) keep RPH is based on carrier local policy | Terminating NS/EP Service Provider: Validates signed RPH (NS/EP NGN-PS process) If validation is successful, Invite is forwarded within terminating network with RPH If validation is not successful, decision to (a) strip RPH or (b) keep RPH is based on carrier local policy If signed TN was expected and not received use info in signed RPH for verified Caller-ID or display TN as verified as a default for RPH call?
ppt [“shaken“]
ppt [“shaken“]
ppt [“shaken“]

## Slide 5: Use Case 2: TN Signed FC+DN Call
Originating WPS
Transit NS/EP NGN-PS Provider
Terminating network
UE
UE
1. Invite
2. Invite
ets.x wps.y
ets.x wps.y
3. Invite
4. Invite
Originating WPS | Transit NS/EP NGN-PS Provider | Terminating NS/EP Service Provider
Handset subscribed for NS/EP NGN-PS and is registered: User initiates FC call (i.e., *272) SP performs normal NS/EP NGN-PS processing (i.e., subscription validation) and populates ets and wps name spaces with provisioned values RPH is signed by WPS SP TN signed by WPS SP (SHAKEN process) | Transit NS/EP NGN-PS Provider: Signed RPH passed unchanged Signed TN passed unchanged | Terminating NS/EP Service Provider: Validates signed RPH (NS/EP NGN-PS process) If validation is successful, Invite is forwarded within terminating network with RPH If validation is not successful, decision to (a) strip RPH or (b) keep RPH is based on carrier local policy Signed TN is verified (SHAKEN process) and displayed accordingly Note: Call information is not provided to CVT (e.g., 3rd party analytics)
ppt [“shaken“]
ppt [“shaken“]
ppt [rph:"auth“]
ppt [rph:"auth“]

## Slide 6: Use Case 3: TN and RPH Signed FC+AN Call
Originating WPS
Originating NS/EP NGN-PS Provider
Transit NS/EP NGN-PS Provider
Terminating NS/EP NGN-PS Provider
UE
UE
1. Invite
2. Invite
ppt [rph:"auth“]
ets.x wps.y2
ets.x wps.y1
ets.x wps.y
ppt [rph:"auth“]
3. Invite
4. Invite
5. Invite
Originating WPS | Originating NS/EP NGN-PS (IXC) Provider | Transit NS/EP NGN-PS Provider | Terminating NS/EP NGN-PS Provider
Handset subscribed for NS/EP NGN-PS and is registered: User initiates FC+AN call (i.e., *272+NCS-GETS) SP performs normal NS/EP NGN-PS processing (i.e., subscription validation) and populates ets and wps name spaces with provisioned values RPH is signed by WPS SP TN Signed (SHAKEN process) | NS/EP NGN-PS Provider: Performs normal NS/EP NGN-PS processing (including PIN validation) and RPH ets and wps name spaces are populated with provisioned values where the wps value is set to the user priority RPH of outgoing SIP Invite is signed using PASSPorT extension and included in a SIP identity header since RPH was changed Received signed TN is discarded Option: Sign new TN in separate identity header or new TN is not signed separately? | Transit NS/EP NGN-PS Provider: May validate the signed RPH to determine whether priority is provided within transit network Signed RPH passed unchanged Signed TN passed unchanged | Terminating NS/EP NGN-PS Provider: Validates signed RPH If validation is successful, Invite is forwarded within Terminating network with the RPH If validation is not successful decision to (a) strip RPH or (b) keep RPH is based on carrier local policy If signed TN was expected and not received use info in signed RPH for verified Caller-ID or display TN as verified as a default for RPH call?
ppt [“shaken“]
ppt [“shaken“]
ppt [“shaken“]
ppt [rph:"auth“]
Note: There may be a Transit provider between the WPS and Originating NS/EP NGN Provider

## Slide 7: Use Case 4: TN and RPH Signed GETS-NT or AN+GETS-PDN Calls
Originating LEC
Originating NS/EP NGN-PS Provider
Transit NS/EP NGN-PS Provider
Terminating NS/EP NGN-PS Provider
UE
UE
1. Invite
2. Invite
ppt [rph:"auth“]
ets.x wps.y
ets.x
ets.x wps.y
ppt [rph:"auth“]
3. Invite
4. Invite
5. Invite
Originating LEC | Originating NS/EP NGN-PS Provider | Transit NS/EP NGN-PS Provider | Terminating NS/EP NGN-PS Provider
LEC is not NGN-PS Service Provider: User initiates GETS-NT or GETS-PDN call Call identified as NS/EP based on dialed digits and routed to NS/EP NGN-PS Service Provider RPH is NOT signed TN Signed (SHAKEN process) | NS/EP Service Provider: Performs normal NS/EP NGN-PS processing, including PIN validation, translation and Caller-ID modification for anonymity and population of the RPH namespaces RPH of outgoing SIP Invite is signed using PASSPorT extension and included in a SIP identity header Received signed TN is discarded Option: Sign new TN in separate identity header or new TN is not signed separately? | Transit NS/EP NGN-PS Provider: May validate the signed RPH to determine whether Invite is forwarded within transit network with RPH If validation is successful, Invite is forwarded within transit network with the RPH If validation is not successful decision to (a) strip RPH or (b) keep RPH is based on carrier local policy | Terminating NS/EP Service Provider: Validates signed RPH If validation is successful, Invite if forwarded within terminating network with RPH If validation is not successful, decision to (a) strip RPH or (b) keep RPH is based on carrier local policy If signed TN was expected and not received use info in signed RPH for verified Caller-ID or display TN as verified as a default for RPH call?
ppt [“shaken“ tn x]
ppt [“shaken“ tn y]
ppt [“shaken“ tn y]

## Slide 8: Use Case 5: TN and RPH Signed GETS-NT or AN+GETS-PDN Calls Terminating in non-NS/EP NGN-PS Network
Originating LEC
Originating NS/EP NGN-PS Provider
Transit NS/EP NGN-PS Provider
Terminating Network
UE
UE
1. Invite
2. Invite
ppt [rph:"auth“]
ets.x wps.y
ets.x
ets.x wps.y
ppt [rph:"auth“]
3. Invite
4. Invite
5. Invite
Originating LEC | Originating NS/EP NGN-PS Provider | Transit NS/EP NGN-PS Provider | Terminating Network
LEC is not NGN-PS Service Provider: User initiates GETS-NT or GETS-PDN call Call identified as NS/EP based on dialed digits and routed to NS/EP NGN-PS Service Provider RPH is NOT signed TN Signed (SHAKEN process) | NS/EP Service Provider: Performs normal NS/EP NGN-PS processing, including PIN validation, translation and Caller-ID modification for anonymity and population of the RPH namespaces RPH of outgoing SIP Invite is signed using PASSPorT extension and included in a SIP identity header Received signed TN is discarded Option: Sign new TN in separate identity header or new TN is not signed separately? | Transit NS/EP NGN-PS Provider: May validate the signed RPH to determine whether Invite is forwarded within transit network with RPH If validation is successful, Invite is forwarded within transit network with the RPH If validation is not successful decision to (a) strip RPH or (b) keep RPH is based on carrier local policy | Terminating Network is NOT NS/EP Service Provider: Terminating network is NOT NS/EP NGN-PS SP: RPH processing and priority treatment not required therefore validation of signed RPH not required If signed TN was expected and not received use of info in signed RPH for verified Caller-ID may not be possible if “rph” ppt is not supported? Should display TN as verified as a default for RPH call?
ppt [“shaken“ tn x]
ppt [“shaken“ tn y]
ppt [“shaken“ tn y]

## Slide 9: Summary of Key Issues
OEC Service Provider Council Discussion
  NS/EP NGN-PS service providers will not include separate identity headers for signed TN and RPH.
  When the SIP RPH is signed, a separate token for the TN will not be included (i.e., an NS/EP NGN-PS provider will replaced a signed TN in a received message with a signed RPH in the outgoing message)
Issue: Terminating Network Handling of signed RPH when signed TN is expected
  Need to specify behavior of a non-NS/EP NGN-PS network expecting to receive a signed TN but receives a signed RPH
Proposal
  Update ATIS-1000074 (SHAKEN) to include statement indicating that if a signed RPH is received and there is no signed TN, the information in the signed RPH should be used for Call Validation Treatment (CVT) (and provide pointer to the RPH Signing standard)

## Slide 10
Thank You