## Slide 1
IPNNI Enterprise Scenarios and Requirements
May 21, 2019
Mary Barnes, iconectiv Industry Solutions
Email: mbarnes@iconectiv.com

## Slide 2: Roles and Responsibilities
TN Provider: SP that has been formally assigned the TNs that the Enterprise (aka TN Customer) is using to make outgoing calls. TN Provider may also serve in the role as OSP.
TN Customer: Entity (e.g.,enterprise) that has been given the authority to use TNs that have been formally allocated to a TN Provider. The TN customer may perform the Authentication function (i.e., add one or more SIP Identity header fields).
Originating SP (OSP): The service provider that handles the outgoing calls at the point at which they are entering the PLMN. The OSP may perform the Authentication function. OSP may also serve in the role as TN Provider.
Reseller SP: TN Customer that serves in the role of an SP providing the use of the TNs to various entities (e.g., call centers, cloud solutions) that behave as enterprises. Reseller SP may also serve in the role of an OSP.
Terminating SP: the SP whose network terminates the call (i.e., arrives at the called party). The terminating SP performs the Verification function.

## Slide 3: Key considerations
There are two aspects to consider in identifying requirements and developing a solution:
  1) Capturing and communicating information that facilitates trace back
  2) Capturing and communicating information that provides additional information (along with analytics) to display meaningful and accurate information to the consumer.
SHAKEN currently uses PASSporT to capture and communicate information for 1) including Attestation and Origid.
Information to support 2) *might* include the Attestation value in the SHAKEN PASSporT determined by the Authentication function. The ‘verstat’ value, determined by the verification function, is intended to directly provide information to support 2) and is communicated to the SIP UA.
Operating and business requirements for the various users (SPs, Enterprises and Resellers) of the SHAKEN Ecosystem are variable
  However, everyone seems to want an Attestation of ‘A’ which makes that field quite binary and it may well be meaningless – i.e., do you put any trust in the information with an Attestation of ‘C’?

## Slide 4: Objectives
Develop a solution proposal that leverages existing (or newly defined) protocol building blocks including:
  SHAKEN PASSporT – usage outlined in ATIS-1000074
  RCD PASSporT – usage not yet applied to SHAKEN as specified in ATIS-1000074.
    Could be used to provide additional information for display.
Consider diverse requirements for each of the roles and deployment models:
  TN Customer with TNSP(s) serving in the role of OSP (one to one model)
  Single TNSP and multiple OSPs.
  TN Customer with multiple TNSPs and single OSP
  Different OSPs for the same TN (e.g., time of day routing)
  Reseller OSP(s) supporting multiple TN Customers

## Slide 5: Basic Requirements for solution specification
The calling party identity of the TN customer must be authenticated and authorized by the Originating SP through some means – direct or indirect
The Terminating SP must be able to process multiple Identity header fields with multiple types of PASSporTs
Must support TN Customers (TNCs) with varying ability to build Identity header fields – minimize impact on TNCs:
  Depends entirely on relationship between TNCs, TNSPs and OSPs

## Slide 6: Scenario (1)
Originating SP (OSP) is the TN Provider (TNSP).
  Originating SP should add a SIP Identity header field with an attestation of “A” signing with STI-certificate
  Originating SP may allow a TN Customer to provide an Identity header field with an RCD PASSport
  Terminating SP receives only Identity header field with a SHAKEN PASSporT.
  Terminating SP may also receive additional Identity header fields with other PASSporTs such as RCD (and Divert).

## Slide 7: Scenario (1a)
Terminating Service
Provider
SP-KMS
STI-CR
STI-AS
STI-VS
STI-CA
SIP UA
SIP UA
Call Server
Call Server
Call Server
TN Customer
1. SIP
INVITE
2. SIP INVITE
4. SIP INVITE
(SHAKEN A)
OSP
3. SIP INVITE
8. SIP INVITE
(verstat, display
stuff)
5. SIP INVITE
SHAKEN A).
CVT
7. Validate
Identity
(TNAuthList+)
6. Get Certificate
TNSP
0. Get/Configure TNs
SPC’s
Assigned to
TN Customers
Assigned TNs
TNSP Assigned TNs
DBs

## Slide 8: Scenario (1b w/RCD)
Terminating Service
Provider
SP-KMS
STI-CR
STI-AS
STI-VS
STI-CA
SIP UA
SIP UA
Call Server
Call Server
Call Server
TN Customer
1. SIP
INVITE
2. SIP INVITE (RCD)
4. SIP INVITE
(RCD, SHAKEN A)
OSP
3. SIP INVITE (RCD)
8. SIP INVITE
(verstat, display
stuff)
5. SIP INVITE
(RCD, SHAKEN A).
CVT
7. Validate
Identity
(TNAuthList+)
6. Get Certificate
TNSP
0. Get/Configure TNs
SPC’s
Assigned to
TN Customers
Assigned TNs
TNSP Assigned TNs
DBs
TNC-AS
TNC-KMS
STI-VS
1.1. SIP INVITE
TN RCD
2.3. Get Certificate
2.1. SIP INVITE (RCD)
STI-CA
STI-CR

## Slide 9: Scenario (2)
Originating SP is not the TN Provider. Originating SP has a direct relationship with the TN Customer.
OSP should not require an Identity header field in the INVITE from the TN customer:
  Originating SP may allow a TN Customer to provide an Identity header field with an RCD PASSport.
  OSP should add a SIP Identity header field with Attestation “A”.
  Terminating SP receives only one Identity header field with a SHAKEN PASSporT.
  Terminating SP may also receive additional Identity header fields with other PASSporTs such as RCD (and Divert).

## Slide 10: Scenario (2a)
Terminating Service
Provider
SP-KMS
STI-CR
STI-AS
STI-VS
STI-CA
SIP UA
SIP UA
Call Server
Call Server
Call Server
TN Customer
1. SIP
INVITE
2. SIP INVITE
4. SIP INVITE
(SHAKEN A)
OSP
3. SIP INVITE
8. SIP INVITE
(verstat, display
stuff)
5. SIP INVITE
SHAKEN A)
CVT
7. Validate
Identity
(SPC, From)
6. Get Certificate
TNSP
0. Get/Configure TNs
SPC’s TNs
Assigned to
TN Customers
Assigned TNs
TNSP Assigned TNs
DBs
7.1 Validate TN
assigned to SPC

## Slide 11: Scenario (2b) – w/ RCD)
Terminating Service
Provider
SP-KMS
STI-CR
STI-AS
STI-VS
STI-CA
SIP UA
SIP UA
Call Server
Call Server
Call Server
TN Customer
1. SIP
INVITE
2. SIP INVITE (RCD)
4. SIP INVITE
(RCD, SHAKEN A)
OSP
3. SIP INVITE
8. SIP INVITE
(verstat, display
stuff)
5. SIP INVITE
(RCD, SHAKEN A)
CVT
7. Validate
Identity
(SPC, From)
6. Get Certificates
TNSP
0. Get/Configure TNs
SPC’s TNs
Assigned to
TN Customers
Assigned TNs
TNSP Assigned TNs
DBs
TNC-AS
TNC-KMS
1.1. SIP INVITE
TN RCD
7.1 Validate TN
assigned to SPC
TNCust-CA
STI-CR
(TNCust)
STI-CR
(TNCust)_

## Slide 12: Scenario (2c) – w/ SHAKEN A from TN Customer – SP Passes)
Terminating Service
Provider
SP-KMS
STI-CR
STI-AS
STI-VS
STI-CA
SIP UA
SIP UA
Call Server
Call Server
Call Server
TN Customer
1. SIP
INVITE
2. SIP INVITE (SHAKEN A)
4. SIP INVITE
(SHAKEN A)
OSP
8. SIP INVITE
(verstat, display
stuff)
5. SIP INVITE
(SHAKEN A).
CVT
7. Validate
Identity
(TNAuthList+)
6. Get Certificate
TNSP
0. Get/Configure TNs
SPC’s TNs
Assigned to
TN Customers
Assigned TNs
TNSP Assigned TNs
DBs
TNC-AS
TNC-KMS
1.1. SIP INVITE
TN RCD
TN Cust-CA
CR (TNCust)
7.1 Validate TN
assigned to SPC
STI-CR
(TNCust)

## Slide 13: Scenario (3)
Originating SP is not the TN Provider & Originating SP has no relationship with the TN Customer.
SIP INVITE may have passed through one or more intermediaries prior to reaching the Originating SP.
If the incoming INVITE contains a SIP Identity header field.
  OSP should verify the Identity in the incoming SIP Invite.
  Incoming INVITE may also include an RCD PASSport
  OSP should add an additional SIP Identity header field to capture “origid” for traceback.
If not authenticated (i.e., no Identity header field in the incoming INVITE or verification fails), the OSP should add a SIP Identity header field with Attestation of “C”.
Terminating SP may receive more than one SIP Identity header field with a SHAKEN PASSporT and should verify each.
Terminating SP may also receive additional Identity header fields with other PASSporTs such as RCD (and Divert).

## Slide 14: Scenario (3a –with RC & SHAKEN A)
Terminating Service
Provider
SP-KMS
STI-CR
STI-AS
STI-VS
STI-CA
SIP UA
SIP UA
Call Server
Call Server
Call Server
TN Customer
1. SIP
INVITE
2. SIP INVITE (RCD, SHAKEN1 A)
4. SIP INVITE
(RCD, SHAKEN2 A,
SHAKEN1 A)
OSP
3. SIP INVITE (RCD)
8. SIP INVITE
(verstat, display
stuff)
5. SIP INVITE
(RCD, SHAKEN2 A, SHAKEN1 A.
CVT
7. Validate
Identity
(TNAuthList1))
6. Get Certificate
TNSP
0. Get/Configure TNs
SPC TNs
Assigned to
TN Customers
Assigned TNs
TNSP Assigned TNs
DBs
TNC-AS
TNC-KMS
1.1. SIP INVITE
TN RCD
STI-CA
STI-CR
STI-VS
2.2. Get Certificate
2.1. SIP INVITE (RCD)
7.1 Validate TN
assigned to SPC

## Slide 15: Scenario (3b) – No Identity or Relationship)
Terminating Service
Provider
SP-KMS
STI-CR
STI-AS
STI-VS
STI-CA
SIP UA
SIP UA
Call Server
Call Server
Call Server
TN Customer
1. SIP
INVITE
2. SIP INVITE
4. SIP INVITE
(SHAKEN C)
OSP
3. SIP INVITE
8. SIP INVITE
(verstat, display
stuff)
5. SIP INVITE
(SHAKEN C).
CVT
7. Validate
Identity
6. Get Certificate
TNSP
0. Get/Configure TNs
SPC TNs
Assigned to
TN Customers
Assigned TNs
TNSP Assigned TNs
DBs

## Slide 16: Solution Options for TN Customers
Two solutions proposed – focus is on certificate acquisition by the TN Customers:
Delegated Certificates
Lemon-Twist (LEveraging MOdels for Enterprise dialiNg - TNauthlist With an enterprise Identity Secured Token)
Solution options are focused only on interface between TNSP and TN customer, specifically defining how the TN Customer, using protocol building blocks, can acquire a certificate for signing PASSporTs to pass information such as RCD and SHAKEN to the OSP
  They don’t define behaviors of the OSP nor the TSP, but rather provide secure, authenticated information that could be used by OSP and TSP

## Slide 17: Delegated Certificate Model
Utilizes delegated certificates as described in RFC 8226 and draft-peterson-:
Adds cross certificates to the model based on RFC 5280:
  SP hosts a CA delegated by one of the STI-CAs:
  Enterprise requests certificate from SP CA
Key advantages:
  Uses standard PKI functions for delegation
Disadvantages:
  Increases complexity:
    Additional fields in certificates
    Additional criteria to be considered and established by the CP/CPS (currently states no cross certificates)
    More complex certificate path validation at the STI-VS
      Increases # certificate chains to manage
    More complex traceback and debugging
  SP now manages a PKI instance

## Slide 18: LEveraging MOdels for Enterprise dialiNg (Lemon) - TNs With an enterprise Identity Secured Token (TWIST) (1)
Based on Trust Authority model developed for STI-PA:
  Introduces a Trust Anchor (TA) logical function for supporting SPs Enterprise customers
  Trust Anchor provides a subset of functionality provided by the STI-PA
  TA supports API for Authority Token Acquisition
A unique identifier is assigned by the SP for the TN Customer:
  Concatenation of SPC with an additional identifier assigned by the SP
SP configures account with the TA with the identifiers
SP provides the Enterprise with credentials to obtain an SPC token from the TA, removing SP/TN Provider from any subsequent interactions
Input to token generation includes SPC+id and TNs
The Trust Anchor may be supported in the STI-PA or by another entity with which the SP has an equivalent trust relationship
for managing SP specific accounts and numbering

## Slide 19: LEveraging MOdels for Enterprise dialiNg (Lemon) – TNs With an enterprise Identity Secured Token (TWIST) (2)
Originating SP does not need to verify the SIP Identity header field added by the enterprise:
  Passes the SIP Identity header field as received from the enterprise
  Originating SP can add an additional SIP Identity header field with attestation ‘A’ depending upon relationship with Enterprise

## Slide 20
Enterprise
Trust Anchor/STI-PA
STI
Certification
Authority
SHAKEN LEMoN TWIST Interfaces
Enterprise Account with TNs for each SPC+id
Authority Token
SPC Token Cert
Protocol/API
Human I/F
DataBase I/F
Service Provider
Credentials for Authority Token API &
URLs for List of STI-CAs
List of CAs
CRL
CRL URL
Authority
Token
SP Codes’ Assigned TNs
DBs

## Slide 21: Summary – LEMoN TWIST
Model is consistent with core SHAKEN:
  Trust is based on secure token provided by the entity that has been given authority over the TNs
  Gives enterprises flexibility in choosing an STI-CA
Reduces burden on SP’s role in certificate acquisition
  Doesn’t require more complex certificate delegation model
Reduces processing burden on originating SP
TN Customer directly interfaces with an STI-CA
More transparent – terminating SP recognizes call as being from an authorized user of SP-x’s TNs – consistent with the “What do we know and how do we know it model”
Enterprise isn’t relegated behind the SP in the SHAKEN ecosystem
No new PKI requirements (no new IETF dependency)
Hosting in the STI-PA simplifies SP account management

## Slide 22: Overall Comparison: Delegated Certificates and Lemon Twist
 | Delegated Certificates | Lemon TWIST | SHAKEN
Who issues Certificate | Delegated CA in TN SP’s domain | Any trusted STI-CA (selected by Enterprise) | Any trusted STI-CA (selected by OSP)
Input for Authority Token acquistion | N/A – TN Cust is pre-approved | SPC+id, TNs | SPC
Challenge-response mechanism | N/A – TN Cust is pre-approved | TN Customer’s Authority token issued by TA | SP’s Authority token issued by the STI-PA

## Slide 23: Functional Impacts: Delegated Certificates and Lemon Twist
 | Delegated Certificates | Lemon TWIST
New SP functionality (KMS) | Delegated CA in TNSP’s domain | Input to trust authority for authority token = SPC+id, TNs (TN Customer)
Certificate generation (KMS and STI-CA) | Requires more complete standardization for delegated certificates for STIR* | Same as SHAKEN
Challenge-response mechanism (KMS and STI-CA) | N/A – TN Cust is pre-approved | Same as SHAKEN
Certificate path validation (STI-VS) | More complex due to delegated (cross) certificates** | Same as SHAKEN
Authentication (STI-AS) | TN Customer adds an Identity header field OSP also adds an Identity header field (unless pre-existing trust relationship) | TN Customer add anSets Attestation to A’
* https://www.ietf.org/id/draft-peterson-stir-cert-delegation-00.txt
** https://mailarchive.ietf.org/arch/msg/stir/YVRfILEUu0yZaHMIMc3hIcEQPug:
“This can be a bit messy when delegating from SPC to TN ranges, but that messiness probably isn’t avoidable.”

## Slide 24: Questions ???