## Slide 1
Rich Call Data Integrity Mechanism

## Slide 2
Problem: Malicious TN Customer could use fake or spoof company name/logo/etc.
Example use case:
TN customer with malicious intent obtains a delegate end-entity cert from its TN Provider
TN customer originates call from TN that is in-scope for the delegate cert TNAuthList (i.e., can’t spoof calling number)
TN Customer populates "rcd" claim with the company name/logo of a different company.
Rich-call-data is rendered to called user with a "green checkmark"
We need a mechanism that enables verifiers to detect when a TN customer includes RCD data that it is not authorized to use.

## Slide 3
Solution: Rich Call Data Integrity procedures defined in draft-ietf-stir-passport-rcd
Subordinate CA
Delegate end-entity Certificate
TNAuthList
  spc: 1234
  range: tn-20,10
JWTClaimConstraints
  mustInclude: "rcdi"
  permittedValues: "sha256-H8BRh…X6xO"
Delegate CA Certificate
TNAuthList
  spc: 1234
  range: tn-10,100
TN Customer
1) Issue delegate end-entity certificate with JWTClaimConstraints object.
Delegate CA cert
Delegate end-entity cert
RCD PASSporT
Protected Header {
… }
Payload {
"dest":{tn-x},
"iat":1443208345,
"orig":{tn-20},
"rcdi":"sha256-H8BRh…X6xO",
"rcd":{"nam": company name,
”icn": <uri to company logo>}
Signature
TN Provider
3) RCD Verification verifies that claims constraints have been met
Procedure
TN Provider issues certificate to TN Customer containing a JWTClaimConstraints object that mandates inclusion of "rcdi" claim with a specific claim value for all PASSporTs signed by this certificate.
RCD Authentication complies with the constraints by including an “rcd” claim with the indicated value.
RCD Verification calculates a digest across the “rcd” claim value, and compares it to the “rcdi” value. A mismatch results in a verification failure.
2) RCD Authentication complies with claims constraint
Use JWTClaimConstraints to mandate inclusion of new "rcdi" claim that contains digest of "rcd" claim