## Slide 1: Simplifying the Full Attestation Enterprise Problem
with a Central TN Database
Dr Peter Brown | STIR/SHAKEN Product Manager January 2020

## Slide 2: STIR/SHAKEN context
STIR/SHAKEN creates a trust relationship between OSP and TSP
  Regardless of the multiple entities through which the SIP traffic must pass
An OSP’s subscribers are in this circle of trust, i.e. they get A-level attestation
  Which requires that the OSP polices its subscribers’ connections
We want to add the OSP’s Enterprise Customers to this circle
  There may be a chain of Enterprises upstream of the OSP’s Customer involved in the initiation of a call
Enterprise
OSP
TSP

## Slide 3: Guiding Principles: Central TN Database
In overview, here we are concerned with a database which
  Records TNs that are assigned to Enterprises
  Is centrally administered, or is synchronized between multiple providers
  May have multiple service bureaus that provide access.
The impact on Enterprises must be minimized
  No requirement for any new network elements
  Ideally, no software upgrades
The complexity for Carriers should be low
Enterprises must be able to port numbers from one Carrier to another
For traceability, it must be possible to identify
  The Enterprise that initiated a call
  The chain of Enterprises through which a call has passed before arriving at an OSP.

## Slide 4: Central TN Database - Definitions
OSP | Originating Service Provider
TSP | Terminating Service Provider
TNSP | TN Service Provider; service provider that owns TNs and distributes to Enterprises
Enterprise | Any non-SP organization involved in VoIP call path
Initiator Enterprise | Enterprise that is permitted to create a SIP INVITE for a TN
Enabler Enterprise | Enterprise that is permitted to pass-through a SIP INVITE for a TN

## Slide 5: Central TN Database – Enterprise identity
Enterprise identity is a crucial element in the CTND approach
Enterprises must be vetted and be provided with a unique Enterprise ID
Envisage a central Enterprise ID repository from which:
Enterprises request IDs
OSPs & TNSPs can validate Enterprise ID interactions
Enterprises can use their ID
When requesting TNs from their TNSP(s)
When establishing their connectivity with their OSP(s)
To login to the Central TN Database to assign their TNs to other Enterprises
Optionally, to login to the CTND to add Rich Call Data that will be used by the OSP.

## Slide 6: Simple Enterprise example – TN assignment
TNSP: | AT&T |  | 
TN Owner: | Santa Barbara FD | Initiator | Expires 12/31/19
AT&T
Verizon
Santa Barbara Fire Department
TNSP
OSP
CTND
703-555-1234
Santa Barbara Fire Department requests TNs from a TNSP.
TNSP records the TN owner in the CTND.
1
2

## Slide 7: Simple Enterprise example – call flow
AT&T
Verizon
Santa Barbara Fire Department
TNSP
OSP
TNSP: | AT&T |  | 
TN Owner: | Santa Barbara FD | Initiator | Expires 12/31/19
CTND
703-555-1234
Santa Barbara FD makes call through an OSP.
OSP uses CNTD to confirm SBFD has permission to use TN.
SIP INVITE
INVITE with A-level PASSport
REST

## Slide 8: Complex Enterprise example – TN assignment
AT&T
Verizon
Santa Barbara Fire Department
TNSP
OSP
Everbridge
Twilio
1
TNSP: | AT&T |  | 
TN Owner: | Santa Barbara FD | Initiator | Expires 12/31/19
CTND
703-555-1234
2
3
4
TN Assignee: | Everbridge | Initiator | Expires 12/7/19
TN Assignee: | Twilio | Enabler | Expires 12/7/19
Santa Barbara FD adds Everbridge as an Initiator for that TN.
Everbridge adds Twilio as an Enabler.

## Slide 9: Complex Enterprise example – Permissions
AT&T
Verizon
Santa Barbara Fire Department
TNSP
OSP
Everbridge
Twilio
1
TNSP: | AT&T |  | 
TN Owner: | Santa Barbara FD | Initiator | Expires 12/31/19
CTND
703-555-1234
2
3
4
TN Assignee: | Everbridge | Initiator | Expires 12/7/19
TN Assignee: | Twilio | Enabler | Expires 12/7/19
Santa Barbara FD adds Everbridge as an Initiator for that TN.
Everbridge adds Twilio as an Enabler.
Initiator can grant Initiator or Enabler permissions
Enabler can only grant Enabler permission

## Slide 10: Complex Enterprise example – call flow
AT&T
Verizon
Santa Barbara Fire Department
TNSP
OSP
Everbridge
Twilio
TNSP: | AT&T |  | 
TN Owner: | Santa Barbara FD | Initiator | Expires 12/31/19
CTND
703-555-1234
TN Assignee: | Everbridge | Initiator | Expires 12/7/19
TN Assignee: | Twilio | Enabler | Expires 12/7/19
REST
INVITE with A-level PASSport
SIP INVITE
SIP INVITE
Everbridge makes call on behalf of SBFD.
Twilio passes call to an OSP.
OSP verifies ownership of TN.
OSP knows the calling party as the last Initiator in the CTND chain. Important for traceback.

## Slide 11: Complex Enterprise example – Alternative routing tree
703-555-1234
Santa Barbara FD
Initiator
Expires 12/31/20
RapidReach
Initiator
Expires 12/1/20
Everbridge
Initiator
Expires 12/1/20
Twilio
Enabler
Expires 12/1/20
Twilio
Enabler
Expires 12/1/10

## Slide 12: Complex Enterprise example – potential SIP attacks
AT&T
Verizon
Santa Barbara Fire Department
TNSP
OSP
Everbridge
Twilio
TNSP: | AT&T |  | 
TN Owner: | Santa Barbara FD | Initiator | Expires 12/31/19
CTND
703-555-1234
TN Assignee: | Everbridge | Initiator | Expires 12/7/19
TN Assignee: | Twilio | Enabler | Expires 12/7/19
REST
INVITE with A-level PASSport
SIP INVITE
SIP INVITE
Everbridge makes call on behalf of SBFD.
Twilio passes call to an OSP.
OSP verifies ownership of TN.
An Initiator who has re-assigned a TN should reject INVITEs from that TN.
An Initiator must police its incoming SIP INVITEs – malicious calls must be rejected, in the same way as we expect SPs to do.
An Enabler must only accept an INVITE from the Enterprise which assigned it the TN.

## Slide 13: Central TN Database – Reputation check on Enterprises
Central TN Database
The Central TN Database can provide a reputation score, based on Analytics, to the OSP
Score based on spoofing rate for calls which have been Initiated/Enabled by an Enterprise
Given a chain of custody of a TN (from the CTND), the OSP can make a decision based on its local policy using:
The reputation of the Initiator Enterprise
The reputations of the subsequent Enabler Enterprises
and hence whether these entities are known to follow best practice on ensuring malicious INVITEs are rejected.

## Slide 14: Central TN Database - Summary
Central TN Database
Enterprises
Register with Enterprise ID database
Use Enterprise ID in interactions with TNSPs and OSPs
If delegating TNs to another VoIP entity, must register that delegation in the CTND
Must police incoming INVITEs to avoid malicious attacks.
OSP
Uses CTND information to confirm whether its Customer has the right to use a delegated TN
Can use CTND information for traceback purposes and, potentially, to retrieve RCD information
Optionally, can use CTND reputation information for analytics purposes.
Stores information about TNs that have been delegated to Enterprises
Each TN is associated with a “chain of custody” of the Enterprises by which it has been delegated
Each of these Enterprises are classified as Initiators or Enablers to allow traceback.
TNSP
Adds information about immediate delegated TNs to CTND.

## Slide 15
Q&A
peter.brown@metaswitch.com