## Slide 1: Out-of-Band STIR/SHAKEN
High Level Discussion of Considerations

## Slide 2: What problem(s) are we trying to solve?
TDM Service Provider Participation
  Enable networks that originate TDM traffic to participate in the SHAKEN ecosystem by posting signed SHAKEN identity-headers to an out-of-band service for retrieval by the terminating network or other trusted entities.
  Enable networks that terminate TDM traffic to participate in the SHAKEN ecosystem by retrieving signed SHAKEN identity-headers from an out-of-band service
TDM Transit Participation
  Enable SIP networks that use TDM interconnect to preserve end-to-end transport of signed SHAKEN identity headers that would otherwise be lost during SIP-to-SS7 interworking.

## Slide 3: What problems are we “not” trying to solve?
SIP In-Band Interworking
  OOB-SHAKEN is not intended to be a replacement/fix for SIP services that fail to fully implement in-band STIR/SHAKEN as defined by IPNNI requirements.

## Slide 4: Guiding Principles (Proposed)
Support “call authentication” for TDM service providers
Support hybrid-technology calls:
  SIP => TDM
  TDM => SIP
  SIP => TDM => SIP
Not impede transition to all-IP (e.g., no lingering functionality or disincentives)
Complement SHAKEN, rather than duplicate or compete:
  Use standard SHAKEN PASSporT
  Interwork with SHAKEN
  Transparent to SIP networks that have implemented SHAKEN
Cost causer = cost payer
  This is a well-established IP-NNI principle that should be considered
Should support extension to full international deployment