Contribution

TITLE: Proposed changes/modification to section 7 of the IP Interconnection document

SOURCE*: Martin Dolly, AT&T

_______________________________

ABSTRACT

This proposes changes/modification to section 7 of the IP Interconnection document.

NOTICE

This is a draft document and thus, is dynamic in nature. It does not reflect a consensus of the ATIS-SIP Forum IP-NNI Task Force and it may be changed or modified. Neither ATIS nor the SIP Forum makes any representation or warranty, express or implied, with respect to the sufficiency, accuracy or utility of the information or opinion contained or reflected in the material utilized. ATIS and the SIP Forum further expressly advise that any use of or reliance upon the material in question is at your risk and neither ATIS nor the SIP Forum shall be liable for any damage or injury, of whatever nature, incurred by any person arising out of any utilization of the material. It is possible that this material will at some future date be included in a copyrighted work by ATIS or the SIP Forum.

* CONTACT: Martin Dolly; email: md3135@att.com; Tel: (609) 903-3360

# NNI Signaling Profile

[i3 Forum]

## SIP Methods and Header Fields

Notations of the codes

For the purpose of the present document clause 6.1.1.4  TS 29.165 v11.5.0 (2012-12) applies as follows:

In the table 6.3 the status codes "m", "o", "c" and "n/a" have the following meanings:

Table 6.3: Key to notation codes for SIP messages

| Notation code | Notation name | Sending side | Receiving side |
| --- | --- | --- | --- |
| m | mandatory | The message shall be supported at II-NNI. Supporting sending a SIP message at the II-NNI means that this message shall be sent over the II-NNI if received from the serving network. It does not imply that network elements inside the serving network or user equipment connected to this network shall support this message. | Supporting receiving a SIP message at the II-NNI means that this message shall be forwarded to the serving network. It does not imply that network elements inside the served network or user equipment connected to this network are supporting this message. |
| o | optional | The message may or may not be supported at II-NNI. The support of the method is provided based on bilateral agreement between the operators. | Same as for sending side. |
| n/a | not applicable | It is impossible to use/support the message. | It is impossible to use/support the message. This message will be discarded by the IBCF. |
| c <integer> | conditional | The requirement on the message ("m", "o" or "n/a") depends on the support of other optional or conditional items. <integer> is the identifier of the conditional expression. | Same as for sending side. |

### SIP Methods

For the purpose of the present document clause 6.1.1.2 TS 29.165 v11.5.0 (2012-12) with the following changes applies.

3GPP TS 24.229 [5] defines the methods allowing an IBCF to interconnect to an IBCF placed in another IM CN subsystem.

The following SIP methods are supported on the II-NNI as defined in table 6.1.

The following table is based on table A.5 and table A.163 of 3GPP TS 24.229 [5] and endorsed for this document:

Editor's Note: Roaming is not included in the initial scope of this document.

Table 6.1: Supported SIP methods

| Item | Method | Ref. | II-NNI | I3Forum II-NNI (non roaming) | I3Forum II-NNI (roaming) |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Sending | Receiving | Sending | Receiving | Sending | Receiving |
| 1 | ACK request | IETF RFC 3261 [13] | m | m | m | m | m | m |
| 2 | BYE request | IETF RFC 3261 [13] | m | m | m | m | m | m |
| 3 | BYE response | IETF RFC 3261 [13] | m | m | m | m | m | m |
| 3 | BYE response | IETF RFC 3261 [13] | m | m | m | m | m | m |
| 4 | CANCEL request | IETF RFC 3261 [13] | m | m | m | m | m | m |
| 5 | CANCEL response | IETF RFC 3261 [13] | m | m | m | m | m | m |
| 5A | INFO request | IETF RFC 6086 [39] | o | o | o | o | o | o |
| 5B | INFO response | IETF RFC 6086 [39] | o | o | o | o | o | o |
| 8 | INVITE request | IETF RFC 3261 [13] | m | m | m | m | m | m |
| 9 | INVITE response | IETF RFC 3261 [13] | m | m | m | m | m | m |
| 9A | MESSAGE request | IETF RFC 3428 [19] | o | o | O | O | o | o |
| 9B | MESSAGE response | IETF RFC 3428 [19] | o | o | O | O | o | o |
| 10 | NOTIFY request | IETF RFC 3265 [20] | c1 | c1 | c1 | c1 | c1 m | c1 m |
| 11 | NOTIFY response | IETF RFC 3265 [20] | c1 | c1 | c1 | c1 | c1 m | c1 m |
| 12 | OPTIONS request | IETF RFC 3261 [13] | m | m | m x1 | m x1 | m x1 | m x1 |
| 13 | OPTIONS response | IETF RFC 3261 [13] | m | m | m x1 | m x1 | m x1 | m x1 |
| 14 | PRACK request | IETF RFC 3262 [18] | m | m | m | m | m | m |
| 15 | PRACK response | IETF RFC 3262 [18] | m | m | m | m | m | m |
| 15A | PUBLISH request | IETF RFC 3903 [21] | c1 | c1 | c1 | c1 | c1 | c1 |
| 15B | PUBLISH response | IETF RFC 3903 [21] | c1 | c1 | c1 | c1 | c1 | c1 |
| 16 | REFER request | IETF RFC 3515 [22] | o | o | o | o | o x2 | o x2 |
| 17 | REFER response | IETF RFC 3515 [22] | o | o | o | o | o x2 | o x2 |
| 18 | REGISTER request | IETF RFC 3261 [13] | c2 | c2 | c2 | c2 | c2 m | c2 m |
| 19 | REGISTER response | IETF RFC 3261 [13] | c2 | c2 | c2 | c2 | c2 m | c2 m |
| 20 | SUBSCRIBE request | IETF RFC 3265 [20] | c1 | c1 | c1 | c1 | c1 m | c1 m |
| 21 | SUBSCRIBE response | IETF RFC 3265 [20] | c1 | c1 | c1 | c1 | c1 m | c1 m |
| 22 | UPDATE request | IETF RFC 3311 [23] | m | m | m | m | m | m |
| 23 | UPDATE response | IETF RFC 3311 [23] | m | m | m | m | m | m |
| c1: In case of roaming scenario, the support of the method is m, else o. c2: In case of roaming scenario, the support of the method is m, else n/a. NOTE: In the above table, m, o and c and n/a have the meanings indicated in table 6.3 x1: Support of OPTIONS in a SIP dialog is mandatory, where support of OPTIONS out of a SIP dialog is optional. Use of OPTIONS outside the dialogue may be used as a keepalive mechanism only based on bilateral agreement. x2: Needed to support CONF service as specified within TS 24.147 [106] Section 5.3.1.5.3 |

Items stroke out in the table above are not in scope of this i3 Forum Release, and items underlined are modifications or additions

Services supporting the following SIP Methods via interconnection II-NNI are out of scope:

- MESSAGE;

- NOTIFY;

- PUBLISH;

- REFER;

- REGISTER; and

- SUBSCRIBE.

Services supporting the following SIP Methods via Roaming II-NNI are out of scope:

- PUBLISH

### SIP Header Fields

##### General

For the purpose of the present document clause 6.1.1.3.0 of TS 29.165 v11.5.0 (2012-12) applies as follows:

The IBCF shall provide the capabilities to manage and modify SIP header fields according to subclause 5.10 and Annex A of 3GPP TS 24.229 [5] with modifications as described in the following subclauses.

##### Trust and no trust relationship

For the purpose of the present document clause 6.1.1.3.1 of TS 29.165 v11.5.0 (2012-12) applies with the following changes of Table 6.2  as follows:

The IBCF acting as exit point applies the procedures described in clause 5.10.2 of 3GPP TS 24.229 [5] before forwarding the SIP signalling to the IBCF acting as entry point. The IBCF acting as entry point applies the procedures described in clause 5.10.3 of 3GPP TS 24.229 [5].

Additionally, in case there is no trust relationship between the two IM CN subsystems connected by II-NNI, the IBCF acting as exit point applies the procedures described in clause 4.4 of 3GPP TS 24.229 [5], before forwarding the SIP signalling.

These procedures may be utilized on a per header field basis to realize overall trust as well as per service level screening of header fields. Trust relationships and trust domains may be defined by inter-operator agreements for individual services and/or individual SIP header fields.

The management of the SIP header fields (if present) over II-NNI in case of a presence or not of a trust relationship between the two interconnected IM CN subsystems is wrapped up in the following table.

Table 6.2: Management of SIP header fields over II-NNI in presence or not of a trust relationship

| Item | Header field | Reference | Trust relationship | Not trust relationship |
| --- | --- | --- | --- | --- |
| 1 | P-Asserted-Identity | IETF RFC 3325 [44] | As specified in 3GPP TS 24.229 [5], clause 4.4 (NOTE 5) | As specified in 3GPP TS 24.229 [5], clause 4.4 (NOTE 5) |
| 2 | P-Access-Network-Info (NOTE 2) | IETF RFC 3455 [24] | As specified in 3GPP TS 24.229 [5], clause 4.4 | As specified in 3GPP TS 24.229 [5], clause 4.4 |
| 3 | Resource-Priority | IETF RFC 4412 [78] | As specified in 3GPP TS 24.229 [5], clause 4.4 | As specified in 3GPP TS 24.229 [5], clause 4.4 |
| 4 | History-Info (NOTE 2) | IETF RFC 4244 [25] | As specified in 3GPP TS 24.229 [5], clause 4.4 | As specified in clause 4.3.3 of RFC 4244 [25] and in 3GPP TS 24.229 [5], clause 4.4 |
| 5 | P-Asserted-Service (NOTE 2) | IETF RFC 6050 [26] | As specified in 3GPP TS 24.229 [5], clause 4.4 (NOTE 3) | As specified in 3GPP TS 24.229 [5], clause 4.4 (NOTE 3) |
| 6 | P-Charging-Vector | IETF RFC 3455 [24] | As specified in 3GPP TS 24.229 [5], clause 5.10 | As specified in 3GPP TS 24.229 [5], clause 5.10 |
| 7 | P-Charging-Function-Addresses (NOTE 4) | IETF RFC 3455 [24] | As specified in 3GPP TS 24.229 [5], clause 5.10 | As specified in 3GPP TS 24.229 [5], clause 5.10 |
| 8 | P-Profile-Key (NOTE 2) | IETF RFC 5002 [64] | As specified in 3GPP TS 24.229 [5], clause 4.4 | As specified in 3GPP TS 24.229 [5], clause 4.4 |
| 9 | P-Private-Network-Indication (NOTE 1) | draft-vanelburg-dispatch-private-network-ind [84] | As specified in 3GPP TS 24.229 [5], clause 4.4 | As specified in 3GPP TS 24.229 [5], clause 4.4 |
| 10 | P-Served-User (NOTE 1, NOTE 2) | IETF RFC 5502 [85] | As specified in 3GPP TS 24.229 [5], clause 4.4 | As specified in 3GPP TS 24.229 [5], clause 4.4 |
| 11 | Reason (in a response) | IETF RFC 6432 [49] | As specified in 3GPP TS 24.229 [5], clause 4.4 | As specified in 3GPP TS 24.229 [5], clause 4.4 |
| 12 | P-Early-Media | IETF RFC 5009 [74] | As specified in 3GPP TS 24.229 [5], clause 4.4 | As specified in 3GPP TS 24.229 [5], clause 4.4 |
| NOTE 1: For a roaming II-NNI, a trust relationship with respect to this header field is required. NOTE 2: This header field is only applicable on a roaming II-NNI whereas for the interconnect NNI it is left unspecified. NOTE 3: In addition, value-dependent operator policies may be applied. NOTE 4: This header field is not applicable at II-NNI. NOTE 5: The handling of the URI parameters "cpc" and "oli", defined in 3GPP TS 24.229 [5] subclause 7.2A.12, is specified in 3GPP TS 24.229 [5], clause 4.4. |

Items stroke out in the table above are not in scope of this i3 Forum Release, and items underlined are modifications or additions.

##### Derivation of applicable SIP header fields from 3GPP TS 24.229 [5]

For the purpose of the present document clause 6.1.1.3.2 of TS 29.165 v11.5.0 (2012-12) applies as follows:

For any method in table 6.1, the SIP header fields applicable on the II-NNI are detailed in the corresponding method tables for the UA role and proxy role sending behavior in Annex A of 3GPP TS 24.229 [5]. Unless other information is specified in the normative part of the present specification, the applicability of header fields at the II-NNI can be derived for each method from the corresponding tables in annex A of 3GPP TS 24.229 [5] as follows:

-	All header fields not present in the corresponding tables in Annex A of 3GPP TS 24.229 or marked as "n/a" in both the "RFC status" and "profile status" columns for the UA role and proxy role sending behaviour of that tables are not applicable at the II-NNI.

NOTE 1:	Operators could choose to apply header fields for other SIP extensions on an II-NNI based on bilateral agreements, but this is outside the scope of the present specification.

-	All header fields which are marked as "o" in at least one of the "RFC status" or the "profile status" profile columns for the sending behaviour in the corresponding UA role and proxy role tables in annex A of 3GPP TS 24.229 [5] and as "n/a" or "o" in the other such columns are applicable at II-NNI based on bilateral agreement between operators.

-	All header fields which are marked as "m" in at least one of the "RFC status" or the "profile status" columns for the sending behaviour in the corresponding UA role or proxy role table in annex A of 3GPP TS 24.229 [5] and as "n/a", "o", or "m" in the other such columns are applicable at the II-NNI.

-	If conditions are specified, they are also applicable at the II-NNI and the above rules are applicable to the "n/a", "o" and "m" values within the conditions.

NOTE 2:	In the above rules, the RFC profile columns are taken into account in order to enable interworking with non-3GPP networks,

An informative summary of SIP header fields to be used over the II-NNI is proposed in annex A.

##### Applicability of SIP header fields on a roaming II-NNI

For the purpose of the present document clause 6.1.1.3.3 of TS 29.165 v11.5.0 (2012-12) applies as follows:

The following SIP header fields are only applicable on a roaming II-NNI:

-	Authentication-Info

-	Authorization

-	P-Associated-URI

-	P-Called-Party-ID

-	P-Preferred-Service

-	P-Profile-Key

-	P-Served-User

-	P-Visited-Network-ID

-	Path

-	Proxy-Authenticate

-	Proxy-Authorization

-	Service-Route

-	WWW-Authenticate

##### Applicability of SIP header fields on a non-roaming II-NNI

For the purpose of the present document clause 6.1.1.5 of TS 29.165 v11.5.0 (2012-12) applies as follows:

The following SIP header fields are only applicable on a non-roaming II-NNI or for the loopback traversal scenario:

-	P-Refused-URI-List

#### Notations of the codes

Moved to Section 7.1.1.1.

#### Modes of signalling

For the purpose of the present document clause 6.1.1.5 of TS 29.165 v11.5.0 (2012-12) applies applies as follows:

Overlap signalling may be used if agreement exists between operators to use overlap and which method to be used, otherwise enbloc shall be used at the II-NNI.

### SDP Protocol

#### General

For the purpose of the present document clause 6.1.2.1 of TS 29.165 v11.5.0 (2012-12) applies as follows:

The functional entity closest to the border of an II-NNI (see reference model in Clause 5) shall provide the capabilities specified for that network element in Annex A.3 of 3GPP TS 24.229 [5].

The SDP bodies shall be encoded as described in IETF RFC 3261 [13] and in IETF RFC 4566 [147].  The offer/answer model with the SDP as defined in IETF RFC 3264 [146] shall be applied.

### Major Capabilities

For the purpose of the present document clause 6.1.3 of TS 29.165 v11.5.0 (2012-12) applies with the following changes in Table 6.1.3.1 and Table 6.1.3.2. as follows:

This subclause contains the major capabilities to be supported over the II-NNI.

The table 6.1.3.1 specifies which capabilities are applicable for II-NNI. The profile status codes within table 6.1.3.1 are defined in table 6.1.3.2. For the "Basic SIP" capabilities part of table 6.1.3.1, the last column "Profile status over II-NNI" specifies the general status of applicability of the IETF RFC 3261 [13] main mechanisms described in the 2nd column "Capability over the Ici".

For the "Extensions to basic SIP" capabilities part, the last column "Profile status over II-NNI" specifies the general status of applicability of the RFC referenced in the 2nd column "Capability over the Ici". If necessary, the applicability of RFCs at the II-NNI level is further detailed in the present Technical Specification.

The columns "Reference item in 3GPP TS 24.229 [5] for the profile status" provide informative references for comparison purposes into the UA and Proxy role major capabilities tables in 3GPP TS 24.229 [5], where the capabilities are defined via additional references.

Table 6.1.3.1: Major capabilities over II-NNI

| Item | Capability over the Ici | Reference item in 3GPP TS 24.229 [5] for the profile status | Profile status over II-NNI | I3Forum Profile status over II-NNI (non-roaming) | I3Forum Profile status over II-NNI (Roaming) |
| --- | --- | --- | --- | --- | --- |
|  |  | UA Role (NOTE 1) | Proxy role (NOTE 2) |  |  |  |
|  | Basic SIP (IETF RFC 3261 [13]) |  |  |  |  |  |
| 1 | registrations | 1, 2, 2A | - | c2 | c2 n/a | c2 m |
| 2 | initiating a session | 2B, 2C, 3, 4 | - | m | m | m |
| 3 | terminating a session | 5 | 3 | m | m | m |
| 4 | General proxy behaviour | - | 4, 5, 14, 15, 19F | n/a | n/a | n/a |
| 5 | Managing several responses due to forking | 9,10 | 6 | m | m | m |
| 6 | support of indication of TLS connections in the Record-Route header | - | 7, 8 | n/a | n/a | n/a |
| 7 | Support of authentication | 7, 8, 8A | 8A | c2 | c2 n/a | c2 m |
| 8 | Timestamped requests (Timestamp header field) | 6 | - | m | m | m |
| 9 | Presence of date in requests and responses (Date header field) | 11 | 9 | m | m o NOTE i3F-2 | m o NOTE i3F-2 |
| 10 | Presence of alerting information data (Alert-info header field) | 12 | 10 | o | o | o |
| 11 | Support and handling of the Require header field for REGISTER and other requests or responses for methods other than REGISTER | - | 11, 12, 13 | m | m | m |
| 12 | Support and reading of the Supported and Unsupported header fields | - | 16, 17, 18 | m | m | m |
| 13 | Support of the Error-Info header field in 3xx - 6xx responses | - | 19 | o | o | o |
| 14 | Support and handling of the Organization header field | - | 19A, 19B | m | m | m |
| 15 | Support and handling of the Call-Info header field | - | 19C, 19D | m | m | m |
| 16 | Support of the Contact header field in 3xx response | - | 19E | m | m | m |
| 16A | Proxy reading the contents of a body or including a body in a request or response |  | 19F | n/a | n/a | n/a |
|  | Extensions to basic SIP |  |  |  |  |  |
| 16B | 3GPP TS 24.237 [131]: proxy modifying the content of a body | n/a | 19G | n/a | n/a | n/a |
| 17 | IETF RFC 6086[39]: SIP INFO method and package framework | 13 | 20 | o | o | o |
| 17A | IETF RFC 6086 [39]: legacy INFO usage | 13A | 20A | o | o | o |
| 18 | IETF RFC 3262 [18]: reliability of provisional responses in SIP (PRACK method) | 14 | 21 | m | m | m |
| 19 | IETF RFC 3515 [22]: the SIP REFER method | 15 | 22 | o | o | o NOTE i3F-1 |
| 20 | IETF RFC 3312 [40] and RFC 4032 [41]: integration of resource management and SIP (Preconditions framework) | 16 | 23 | o | o | o |
| 21 | IETF RFC 3311 [23]: the SIP UPDATE method | 17 | 24 | m | m | m |
| 22 | IETF RFC 3313 [42]: SIP extensions for media authorization (P-Media-Authorization header field) | 19 | 26 | n/a | n/a | n/a |
| 23 | IETF RFC 3265 [20]: SIP specific event notification (SUBSCRIBE/NOTIFY methods) | 20, 21, 22, 23 | 27, 28 | c1 | c1 o | c1 m |
| 24 | IETF RFC 3327 [43]: session initiation protocol extension header field for registering non-adjacent contacts (Path header field) | 24 | 29 | c2 | c2 n/a | c2 m |
| 25 | IETF RFC 3325 [44]: private extensions to the Session Initiation Protocol (SIP) for network asserted identity within trusted networks | 25 | 30 | c4 | c4 | c4 |
| 26 | IETF RFC 3325 [44]: the P-Preferred-Identity header field extension | - | - | n/a | n/a | n/a |
| 27 | IETF RFC 3325 [44]: the P-Asserted-Identity header field extension | - | - | c4 | c4 | c4 |
| 28 | IETF RFC 3323 [34]: a privacy mechanism for the Session Initiation Protocol (SIP) (Privacy header field) | 26, 26A, 26B, 26C, 26D, 26E, 26F, 26G, 26H | 31, 31A, 31B, 31C, 31D, 31E, 31F, 31G, 31H | m | m | m |
| 29 | IETF RFC 3428 [19]: a messaging mechanism for the Session Initiation Protocol (SIP) (MESSAGE method) | 27 | 33 | o | o | o |
| 30 | IETF RFC 3608 [45]: session initiation protocol extension header field for service route discovery during registration (Service-Route header field) | 28 | 32 | c2 | c2 n/a | m |
| 31 | IETF RFC 3486 [46]: compressing the session initiation protocol | 29 | 34 | n/a | n/a | n/a |
| 32 | IETF RFC 3455 [24]: private header extensions to the session initiation protocol for the 3rd-Generation Partnership Project (3GPP) | 30 | 35 | o | o | o |
| 32A | IETF RFC 3325 [44]: act as first entity within the trust domain for asserted identity | 30A | 30A | n/a | n/a | n/a |
| 32B | IETF RFC 3325 [44]: act as entity within trust network that can route outside the trust network | 30B | 30B | n/a | n/a | n/a |
| 32C | IETF RFC 3325: act as entity passing on identity transparently independent of trust domain | 30C | 30C | n/a | n/a | n/a |
| 33 | IETF RFC 3455 [24]: the P-Associated-URI header field extension | 31 | 36 | c2 | c2 n/a | c2 m |
| 34 | IETF RFC 3455 [24]: the P-Called-Party-ID header field extension | 32 | 37 | c2 | c2 n/a | c2 m |
| 35 | IETF RFC 3455 [24]: the P-Visited-Network-ID header field extension | 33 | 38, 39 | c2 | c2 n/a | c2 m |
| 36 | IETF RFC 3455 [24]: the P-Access-Network-Info header field extension | 34 | 41, 42, 43 | c4 | c4 n/a | c4 o NOTE i3F-2 |
| 37 | IETF RFC 3455 [24]: the P-Charging-Function-Addresses header field extension | 35 | 44, 44A | n/a | n/a | n/a |
| 38 | IETF RFC 3455 [24]: the P-Charging-Vector header field extension | 36 | 45, 46 | c1 | c1 o | c1 m |
| 39 | IETF RFC 3329 [47]: security mechanism agreement for the session initiation protocol | 37 | 47 | n/a | n/a | n/a |
| 39A | draft-dawes-dispatch-mediasec-parameter-03 [137]: Capability Exchange for Media Plane Security | 37A | 47A | n/a | n/a | n/a |
| 40 | IETF RFC 3326 [48]: the Reason header field for the session initiation protocol | 38 | 48 | o | o | o |
| 41 | IETF RFC 6432 [49]: carrying Q.850 codes in reason header fields in SIP (Session Initiation Protocol) responses | 38A | 48A | c4 | c4 | c4 |
| 42 | IETF RFC 3581 [50]: an extension to the session initiation protocol for symmetric response routeing | 39 | 49 | o | o | o |
| 43 | IETF RFC 3841 [51]: caller preferences for the session initiation protocol (Accept-Contact, Reject-Contact and Request-Disposition header fields) | 40, 40A, 40B, 40C, 40D, 40E, 40F | 50, 50A, 50B, 50C, 50D, 50E, 50F | m | m | m |
| 44 | IETF RFC 3903 [21]: an event state publication extension to the session initiation protocol (PUBLISH method) | 41 | 51 | c1 | c1 | o NOTE i3F-2 |
| 45 | IETF RFC 4028 [52]: SIP session timer (Session-Expires and Min-SE headers) | 42 | 52 | m | m o NOTE i3F-2 | m o NOTE i3F-2 |
| 46 | IETF RFC 3892 [53]: the SIP Referred-By mechanism | 43 | 53 | m | m | m NOTE i3F-1 |
| 47 | IETF RFC 3891 [54]: the Session Initiation Protocol (SIP) "Replaces" header | 44 | 54 | o | o | o NOTE i3F-1 |
| 48 | IETF RFC 3911 [55]: the Session Initiation Protocol (SIP) "Join" header | 45 | 55 | o | o | o NOTE i3F-1 |
| 49 | IETF RFC 3840 [56]: the callee capabilities | 46 | 56 | o | o | o |
| 50 | IETF RFC 4244 [25]: an extension to the session initiation protocol for request history information (History-Info header field) | 47 | 57 | o | o | o |
| 51 | IETF RFC 5079 [57]: Rejecting anonymous requests in the session initiation protocol | 48 | 58 | o | o | o |
| 52 | IETF RFC 4458 [58]: session initiation protocol URIs for applications such as voicemail and interactive voice response (NOTE 3) | 49 | 59 | o | o | o |
| 53 | IETF RFC 4320 [59]: Session Initiation Protocol's (SIP) non-INVITE transactions | 50 | 61 | m | m | m |
| 54 | IETF RFC 4457 [60]: the P-User-Database private header field extension | 51 | 60 | n/a | n/a | n/a |
| 55 | IETF RFC 5031 [61]: a uniform resource name for services | 52 | 62 | n/a | n/a | n/a |
| 56 | IETF RFC 5627 [62]: obtaining and using GRUUs in the Session Initiation Protocol (SIP) | 53 | 63 | c1 | c1o | c1 m |
|  | Void |  |  |  |  |  |
| 58 | IETF RFC 4168 [27]: the Stream Control Transmission Protocol (SCTP) as a Transport for the Session Initiation Protocol (SIP) | 55 | 65 | o | o | o |
| 59 | IETF RFC 5002 [64]: the SIP P-Profile-Key private header field extension | 56 | 66, 66A, 66B | c3 | c3 n/a | c3 o |
| 60 | IETF RFC 5626 [65]: managing client initiated connections in SIP | 57 | 67 | c1 | c1o | c1 m |
| 61 | IETF RFC 5768 [66]: indicating support for interactive connectivity establishment in SIP | 58 | 68 | n/a | n/a | n/a |
| 62 | IETF RFC 5365 [67]: multiple-recipient MESSAGE requests in the session initiation protocol | 59 | 69 | o if 29, else n/a | o if 29, else n/a | o if 29, else n/a |
| 63 | draft-ietf-sipcore-location-conveyance-08 [68]: SIP location conveyance (Geolocation header) | 60 | 70, 70A, 70B | m | m | m |
| 64 | IETF RFC 5368 [69]: referring to multiple resources in the session initiation protocol | 61 | 71 | o if 19, else n/a | o if 19, else n/a | o if 19, else n/a |
| 65 | IETF RFC 5366 [70]: conference establishment using request-contained lists in the session initiation protocol | 62 | 72 | o | o | o |
| 66 | IETF RFC 5367 [71]: subscriptions to request-contained resource lists in the session initiation protocol | 63 | 73 | o if 23, else n/a | o if 23, else n/a | o if 23, else n/a |
| 67 | IETF RFC 4967 [72]: dialstring parameter for the session initiation protocol uniform resource identifier | 64 | 74 | c2 | c2 n/a | c2 m |
| 68 | IETF RFC 4964 [73]: the P-Answer-State header extension to the session initiation protocol for the open mobile alliance push to talk over cellular | 65 | 75 | o | o | o |
| 69 | IETF RFC 5009 [74]: the SIP P-Early-Media private header field extension for authorization of early media | 66 | 76 | c4 | c4 | c4 |
| 70 | IETF RFC 4694 [75]: number portability parameters for the ‘tel’ URI | 67, 67A, 67B | 77, 77A, 77B | o | o | o |
| 72 | IETF RFC 4411 [77]: extending the session initiation protocol Reason header for preemption events | 69 | 79 | o | o | o |
| 73 | IETF RFC 4412 [78]: communications resource priority for the session initiation protocol? (Resource-Priority header field) | 70, 70A, 70B | 80, 80A, 80B | o | o | o |
| 74 | IETF RFC 5393 [79]: addressing an amplification vulnerability in session initiation protocol forking proxies | 71 | 81 | m | m | m |
| 75 | IETF RFC 5049 [80]: the remote application identification of applying signalling compression to SIP | 72 | 82 | n/a | n/a | n/a |
| 76 | IETF RFC 5688 [81]: a session initiation protocol media feature tag for MIME application sub-types | 73 | 83 | c1 | c1 o | c1 m |
| 77 | IETF RFC 6050 [26]: Identification of communication services in the session initiation protocol | 74 | 84, 84A | o | o | o |
| 78 | IETF RFC 5360 [82]: a framework for consent-based communications in SIP? | 75, 75A, 75B | 85 | o | o | o |
| 79 | draft-johnston-sipping-cc-uui-09 [83]: transporting user to user information for call centers using SIP? | 76 | 86 | c1 | c1 o | c1 m |
| 79A | draft-ietf-cuss-sip-uui-isdn [83A]: Interworking ISDN Call Control User Information with SIP | 76A | n/a | c1 | c1 o | c1 m |
| 80 | draft-vanelburg-dispatch-private-network-ind-01 [84]: The SIP P-Private-Network-Indication private-header (P-Header) | 77 | 87 | c1 | c1 | c1 |
| 81 | IETF RFC 5502 [85]: the SIP P-Served-User private header | 78 | 88 | c2 | c2 n/a | c2 m |
| 83 | draft-dawes-sipping-debug-04 [87]: the P-Debug-ID header extension | 80 | 90 | o | o | o |
| 84 | IETF RFC 6228 [88]: the 199 (Early Dialog Terminated) response code | 81 | 91 | m | m | m |
| 85 | IETF RFC 5621 [89]: message body handling in SIP | 82 | 92 | m | m | m |
| 86 | IETF RFC 6223 [90]: indication of support for keep-alive | 83 | 93 | o | o | o |
| 87 | IETF RFC 5552 [91]: SIP Interface to VoiceXML Media Services | 84 | 94 | n/a | n/a | n/a |
| 88 | IETF RFC 3862 [92]: common presence and instant messaging (CPIM): message format | 85 | 95 | o | o | o |
| 89 | IETF RFC 5438 [93]: instant message disposition notification | 86 | 96 | o | o | o |
| 90 | IETF RFC 5373 [94]: requesting answering modes for SIP (Answer-Mode and Priv-Answer-Mode header fields) | 87 | 97, 97A | o | o | o |
|  | Void |  |  |  |  |  |
| 92 | IETF RFC 3959 [96]: the early session disposition type for SIP | 89 | 99 | o | o | o |
| 93 | IETF RFC 4244 [97]: delivery of Request-URI targets to user agents | 90 | 100 | n/a | n/a | n/a |
| 94 | draft-kaplan-dispatch-session-id-00 [124]: The Session-ID header | 91 | 101 | o | o | o |
| 95 | IETF RFC 6026 [125]: correct transaction handling for 200 responses to Session Initiation Protocol INVITE requests | 92 | 102 | m | m | m |
| 96 | IETF RFC 5658 [126]: addressing Record-Route issues in the Session Initiation Protocol (SIP) | 93 | 103 | o | o | o |
| 97 | IETF RFC 5954 [127]: essential correction for IPv6 ABNF and URI comparison in IETF RFC 3261 [13] | 94 | 104 | m | m | m |
| 98 | IETF RFC 4488 [135]: suppression of session initiation protocol REFER method implicit subscription | 95 | 105 | m if 19, else n/a | m if 19, else n/a | m if 19, else n/a |
| 99 | draft-ietf-salud-alert-info-urns [136]: Alert-Info URNs for the Session Initiation Protocol | 96 | 106 | o | o | o |
| 100 | Subclause 3.1 of 3GPP TS 24.229: multiple registrations | 97 | 107 | c2 | c2 n/a | c2 m |
| 101 | IETF RFC 5318 [141]: the SIP P-Refused-URI-List private-header | 98 | 108 | c5 | c5 | c5 n/a |
| 102 | IETF RFC 4538 [140]: request authorization through dialog Identification in the session initiation protocol (Target-Dialog header field) | 99 | 109 | o | o | o |
| 103 | draft-holmberg-sipcore-proxy-feature [143]: indication of features supported by proxy | 100 | 110 | o | o | o |
| 104 | IETF RFC 6140: registration of bulk number contacts | 101 | 111 | c2 | c2 n/a | c2 m |
| 105 | IETF RFC 6230: media control channel framework | 102 | 112 | o | o | o |
| 105A | 3GPP TS 24.229 [5]: S-CSCF restoration procedures | 103 | 113 | c3 | c3 n/a | c3 o |
| 106 | RFC 6357 [164] SIP overload control | 104 | 114 | o | o | o |
| 107 | draft-ietf-soc-overload-control [165] feedback control | 104A | 114A | o | o | o |
| c1: m in case of roaming II-NNI, else o c2: m in case of roaming II-NNI, else n/a c3: o in case of roaming II-NNI, else n/a c4: m in case of trust relationship between the interconnected networks, else n/a c5: o in case of non-roaming II-NNI and loopback traversal scenario, else n/a NOTE 1: The item numbering corresponds to the one provided in table A.4 in [5]. NOTE 2: The item numbering corresponds to the one provided in table A.162 in [5]. NOTE 3: A common URI namespace is required to apply this feature on the II-NNI. NOTE i3F-1: Needed to support CONF service as specified within TS 24.147 [106] Section 5.3.1.5.3 NOTE i3F-2:. Item 9: Date header is of no use for basic voice service, which is the scope of the document, as it is globally considered less reliable with regards to locally registered timestamp. Furthermore it's not commonly used for any post-processing (charging, reporting, …) so it's more appropriate to leave it as an optional item. Item 36; this capability is optional due to possible unsecure relationship via public Internet, Item: 44: as shown is Sec. 6.1.1.2.the PUBLISH method is out-of-scope at Interconnection II-NNI Item 45: SIP Session Timer as specified in RFC 4028 is meant to be an end-to-end per-session keepalive mechanism which can result meaningless if there is any node (B2BUA, ASs,...) in the chain, re-generating SIP signalling so interrupting the signalling transparency, as it is common in real environments. It’s more appropriate not to mandate it. |

Items stroke out in the table above are not in scope of this i3 Forum Release, and items underlined are modifications or additions.

Table 6.1.3.2: Key to notation codes for major capabilities

| Notation code | Notation name | Explanation |
| --- | --- | --- |
| M | mandatory | The capability shall be supported at II-NNI. SIP message relating to this capability shall be sent over the II-NNI if received from the serving network, unless they also make use of other unsupported capabilities. SIP headers or other information elements relating to this capability shall be passed over the II-NNI if received from the sending side. This does not imply that network elements inside the serving network or served network or user equipment connected to these networks shall support this capability. |
| O | optional | The capability may or may not be supported at II-NNI. The support of the capability is provided based on bilateral agreement between the operators (i.e. Service Provider and/or carriers according to i3Forum terminology). |
| n/a | not applicable | It is impossible to use/support the capability at the II-NNI. |
| c <integer> | conditional | The support of the capability ("m", "o" or "n/a") depends on the support of other optional or conditional items. <integer> is the identifier of the conditional expression. |

## Control Plane Transport

### General

For the purpose of the present document clause 6.2.1 of TS 29.165 v11.5.0 (2012-12) applies as follows:

The control plane transport of the II-NNI shall comply with clause 4.2A of 3GPP TS 24.229 [5].Support of SCTP as specified in IETF RFC 4168 [27] is optional for an IBCF connected by II-NNI. Nevertheless this option is favourable if the operators would like to improve reliability over the Ici.

## SIP Timers

For the purpose of the present document clause 6.3 of TS 29.165 v11.5.0 (2012-12) applies as follows:

Table 6.3.1 shows values of SIP timers that should be supported at II-NNI. It contains the following items:

-	the first column, titled "SIP Timer", shows the timer names as defined in IETF RFC 3261 [13];

-	the second column reflects the timer meaning as defined in IETF RFC 3261 [13];

-	the third column reflects the reference to the proper section in the IETF RFC 3261 [13] and in 3GPP TS 24.229 [5] and

-	the final column lists the values recommended for the functional entities closest to the border of an II-NNI (see reference model in clause 5).

Table 6.3.1 reports information from 3GPP TS 24.229 [5], table 7.7.1. Values between IM CN subsystem elements shown in the second column in 3GPP TS 24.229 [5], table 7.7.1 are applicable for the II-NNI and are reported in the fourth column of table 6.3.1. If there are any differences between table 6.3.1 and 3GPP TS 24.229 [5], table 7.7.1, the information within 3GPP TS 24.229 [5], table 7.7.1 is applicable.