## Slide 1
Resolving ATIS-1000085 Editor's Note
David Hancock – Nov 14, 2021

## Slide 2: Resolution of the ATIS-1000085.v002 Editor’s Note
Editor’s note says…
  "Editor’s note: Update note below and paragraph above to say that for the case where “div” verification receives a stale PASSporT, it still conveys the received PASSporTs on to the retarget-to TSP. Consider the case where the INVITE is retargeted by end-entity device.”
Proposed resolution  add the following requirement to the 085 "div" authentication procedure
  "The STI-AS shall not perform "div" authentication for a retargeting event if the STI-VS that verified the terminating INVITE request prior to retargeting detected that the outermost PASSporT was stale…"

## Slide 3: Here is the sequence where the above new requirement applies
A SHAKEN SP, playing the role of TSP, receives a terminating INVITE request,
The SP invokes the STI-VS to verify the PASSporT(s) contained in the received INVITE,
The STI-VS detects that the outermost PASSporT is stale,
The INVITE is retargeted by a terminating call feature,
The SP, now playing the role of OSP for the retargeted leg of the call, must not perform "div" authentication because step-3 detected that the outermost PASSporT was stale.
Question
  Should we specify how the information is conveyed from step-3 to step-5 to meet this new requirement?
  If yes, what is the mechanism?

## Slide 4: Three options
Leave the mechanism unspecified
  Since this mechanism is internal to the SP, the SP is free to choose a proprietary mechanism
  E.g., convey info via new private header field or new private PAI header parameter
Use the already-defined verstat parameter
  In step-5 of the sequence, div authentication is done only if …
    The retargeted INVITE contains a shaken Identity header and zero or more div Identity headers, and
    Verstat=TN-Validation-Passed
  One issue with using verstat – it does not support div authentication for INVITE containing a valid shaken PASSporT with attest = B or C (only an issue during div transition period)
    Retargeted INVITE with shaken attest B or C results in verstat=No-TN-Validation, and we’d like to do div authentication
    During div transition period, a broken chain of authority from shaken dest to R-URI also results in verstat=No-TN-Validation, and we must skip div authentication in this case because it would incorrectly "fix" the broken chain
    Maybe the authentication service can distinguish between a) and b), but it’s complicated
Define a new header or PAI parameter to convey this information
  E.g., define something in 3gpp TS 24.229

## Slide 5: Simplifying div authentication
A nice side effect of all three options is… they simplify div authentication of in-network retarget events
  The STI-AS knows explicitly when to perform div authentication
    The INVITE contains a shaken PASSporT plus zero or more div PASSporTs, and
    The verstat (or the new parameter) indicates that the shaken/div PASSporTs were valid before retarget
  The identity of the retargeting entity is unambiguous
    It’s the TN identified by the outermost PASSporT dest claim
    No need to rely on the retargeting feature populating the Diversion or History-Info headers correctly
  This also enables the TS 24.229 div authentication procedures to authenticate multiple intra-network retargets with a single div Identity header
Note, these solution options apply only to in-network retargeting cases and should not be used for INVITEs retargeted by an untrusted end-entity device; i.e., a shaken SP should not honor verstat (or the new parameter) received from an end-entity device.

## Slide 6
PAI: TN-a; verstat=passed
Identity: shaken PASSporT {
orig/dest=a/b }
[6] INVITE TN-c
To: TN-b,
PAI: TN-a; verstat=passed
Identity: shaken PASSporT {
orig/dest=a/b
iat=3 minutes old }
Identity: div PASSporT {
orig/div/dest=a/b/c }
To: TN-b,
PAI: TN-a; verstat=passed
Identity: shaken PASSporT {
orig/dest=a/b }
PAI: TN-a;
verstat=passed
…
Orig IMS
STI-AS
Example of verstat-based option
[7] INVITE TN-c
[8] INVITE TN-c
Peering Partner
Authentication Procedure:
Since [7]INVITE contains a shaken PASSporT and verstat=TN-Validation-Passed, the STI-AS can conclude that …
The INVITE has just been retargeted, and
The shaken PASSporT was verified by the home network STI-VS and was found to be valid before retargeting (i.e., even though the shaken PASSporT is now stale, it is still valid)
Therefore, the STI-AS also knows that…
It should do div authentication for the retargeting event, and
The shaken PASSporT "dest" claim contains the retargeting TN to be populated in the div PASSporT "div" claim
(no need to rely on History-Info or Diversion header)
logic
[1] INVITE TN-b
To: TN-b, PAI: TN-a
Identity: shaken PASSporT {
orig/dest=a/b
attest=A. }
Term IMS
STI-VS
App Server
consultive xfer
(say, they talk for 10 minutes before transfer)
[4] INVITE TN-b
[5] INVITE TN-c
PAI: TN-a; verstat=passed
Identity: shaken PASSporT {
orig/dest=a/b }
PAI: TN-a;
Identity: …
[2] INVITE TN-b
PAI: TN-a; verstat=passed,
Identity: …
[3] INVITE TN-b